## Slide 1: ETRSS-1 Power Supply Subsystem Design
DFH SATELLITE CO.,LTD
February, 2019

## Slide 2
PSS Power Supply System
SA Solar Array
PCDU Power Control/Distribution Unit
BOL Beginning of Life
EOL End of Life
DTS Data Transmission system
GS Ground station
DOD Depth of Discharging
BMU Battery Management Unit
Abbreviations

## Slide 3
Concept and Function
Work principles of PSS
Power balance analysis
OUTLINES
Compositions of PSS
Telemetries and Tele-commands

## Slide 4: Concept and Function
Power Supply System, PSS for short, could be directly equated with the heart of the satellite.
PSS
Function
&Concept
PSS generates，reserves, transforms, regulates and distributes the electrical power on satellite.
PSS carries out the conversion of the light energy or chemical energy into electrical energy by means of certain physical change or chemical change.
PSS takes on the power supply and distribution for the platform and payloads during the testing, launching and orbiting.

## Slide 5
Concept and Function
Power Plant
Transformer Substation
Networks
On the Ground
On the Satellite
Power Control/Distribution Unit
Batteries
Cables

## Slide 6
Technical Specification
Power Bus Number
Voltage of Power Bus
Output power
A single primary power bus is configured.
Primary power bus: +23V ~ +29V
151W at the end of life (EOL)
Type of Voltage
Non-regulated power bus
Concept and Function

## Slide 7
Concept and Function
Work principles of PSS
Power balance analysis
OUTLINES
Compositions of PSS
Telemetries and Tele-commands

## Slide 8: Compositions of PSS
A Solar Array-battery united electrical power system has been adopted.
PSS working Principle
When the output current of solar-arrays is greater than load currents , the output power of solar-arrays is supplied to loads and charged to batteries simultaneously.
When the output current of solar-array is greater than the sum of the load currents and charging current, the redundant energy will be shunted by shunt regulators after charging and power supply.
When the output current of solar-arrays is less than load currents in light, the loads will be supplied by the joint-power supply consisted of solar-arrays and batteries.
Light

## Slide 9: Compositions of PSS
PSS working Principle
Umbra
Since the solar-arrays have no output power in umbra, the loads will be supplied by batteries totally.
.
Launching
There will be no power supply by batteries or solar arrays during launching and orbiting before the expansion of solar-array.
Charge
Discharge
Shunt

## Slide 10: Compositions of PSS ( Solar Array)
Solar energy
Electric energy
photovoltaic conversion
Composition
The whole solar-arrays are composed of many solar cells by series connection and parallel connection compound used in order to obtain voltage and current required.
Solar cell type
Solar Array size
Triple-junction GaAs solar cell
Three solar panels --- one panel for surface-mounted and two fixed solar wings with one panel for each other
Wing number
The total area of the whole solar-arrays is 0.70m that could meet the power requirements.
2

## Slide 11
Compositions of PSS ( Battery)
The structure of batteries is composed of several rechargeable battery cells to gain the voltage and current needed.
Cell number
Battery cell type
Lithium-ion battery
7 cells
10 Ah
Higher power and energy density
Wider temperature range
Higher charging efficiency and better durability
7 cells series connection
Total capacity 10 Ah.
Battery capacity

## Slide 12
Compositions of PSS ( Battery)

## Slide 13
Compositions of PSS ( PCDU)
PCDU: Power Control / Distribution Unit
Function
Composition
To control electrical power distribution to the other subsystems during the mission life.
 To support power requirements for average and peak electrical load.
 To interconnect all equipment and subsystems.
6 Standard PC104 boards: Power shunting board
Power interface board
Power sub-computer boards
Power distribute boards
All these boards are integrated in a PC104 stackable structure.

## Slide 14
Compositions of PSS

## Slide 15
Concept and Function
Compositions of PSS
Power balance analysis
OUTLINES
Work principles of PSS
Telemetries and Tele-commands

## Slide 16
Work principles of PSS
Battery charge
A constant-current to constant-voltage charging method, CC-CV for short, has been adopted for the lithium ion batteries.
Constant Current
Constant
Voltage
Charging will be stopped.
C C
C V
END
Charging voltage of the single cell has
reached a predesigned voltage, such as 4.0V.
A certain small charging current predesigned has been reached.

## Slide 17
Battery charge
Over-charge must be forbidden during the lithium ion batteries charging.
Disadvantage
Lead to the gas production and temperature increase created by decomposition of organic electrolyte inside batteries.
Cause the increase in pressure inside the battery and more seriously, an explosion may take place.
Work principles of PSS

## Slide 18
V
1
2
3
4
5
6
7
The cell will be a serious imbalance compared with other cells after many charging discharge cycles.
The overcharge method could not be used to reach the balance between battery cells.
A balance charging control circuit in battery charge regulator is adopted to ensure the performance balance.
Battery balance
Work principles of PSS

## Slide 19
Battery discharge
Change the lattice of structure of the cathode materials
Oxidize the current collectors of negative electrode
Result in performance degradation and conductivity decreasing
Over-discharge still would not be allowed.
Disadvantage
Work principles of PSS

## Slide 20
Discharging
Strategy
When the voltage of battery cell is less than a certain predesigned value, such as 3.0V, the batteries will be disconnected from the power bus to stop discharging by control circuit.
Specification
The smaller the discharge of depth is, the longer the life of batteries has.
In order to ensure the life time of the lithium ion batteries on the satellite, we should pay much attention to the DOD with the requirement of less than 30%.
Work principles of PSS

## Slide 21
Direct-current power distribution.
A kind of sectional power supply has been adopted.
Switch control
power distribution
The equipments should be powered on by commands after the satellite is powered on, which include AOCS, DTS and CS.
Direct power
distribution
The equipments will be powered on as long as the satellite is powered on, which include PDU, the equipments in OBDH and TT&C.
Work principles of PSS
Distribution

## Slide 22
Work principles of PSS
Energy security mode
Parameters
Battery Voltage
Battery Capacity
Condition 1: Battery Voltage ≤ Batt_Voltage_Alarm_ THRESHOLD (Default value 25.2V)and the time of duration ≥ 30s.
Condition 2: Battery Capacity ≤ Batt_Capacity_Alarm_ THRESHOLD (Default value 6Ah)and the time of duration ≥ 30s.

## Slide 23
Concept and Function
Compositions of PSS
Work principles of PSS
OUTLINES
Power balance analysis
Telemetries and Tele-commands

## Slide 24
Power balance analysis
Purpose
The necessary condition and important guarantee of the satellite working reliability
On the premise of the designs of solar-arrays and batteries, a good PSS would be judged by energy balance analysis whether it is in the state of energy balance or not in one or some orbits.

## Slide 25
In umbra: The loads get the electrical power by battery discharging.
In light : The electric power generated by solar arrays will be used for power supply and battery charging which has been consummated during the umbra.
Lead to the battery over-discharge.
Result in performance degradation and conductivity decreasing
Cause the abnormal situation of the equipments because of the energy shortage.
Power balance analysis
Non-balance
Disadvantage

## Slide 26
At the end of life, during the longest time of umbra, when one battery cell is invalid, the DOD (Depth of Discharging)of the batteries should not be more than 30%.
Conditions
During the shortest time of light, the output power of solar-arrays should not only be enough for the loads power, charging power and power loss in circuits, but also have some power margin.
Power balance analysis

## Slide 27
Modes | Discharging Capacity (Ah) |  | Need to charge capacity (Ah) | Chargeable capacity (Ah) | Capacity margin (Ah) | Depth of discharge (%) | Balance
 | Umbra | Light |  |  |  |  | 
Long-term | 1.62 | 0 | 1.62 | 2.97 | 1.35 | 16.20% | YES
Record | 1.62 | 0.18 | 1.80 | 2.33 | 0.53 | 18.03% | YES
Replay in light | 1.62 | 0.46 | 2.08 | 2.24 | 0.16 | 20.80% | YES
Replay in umbra | 2.12 | 0 | 2.12 | 2.97 | 0.75 | 21.21% | YES
Record and Replay | 1.62 | 0.26 | 1.88 | 2.52 | 0.64 | 18.84% | YES
Real-time | 1.62 | 0.26 | 1.88 | 2.52 | 0.64 | 18.84% | YES
Power balance analysis
Long-term: SA sun-pointing
Operation modes: SA earth-pointing

## Slide 28
Requirement：one circle power balance
Power balance analysis
Chargeable capacity calculation
Chargeable power under short-term load condition
Chargeable power under long-term load condition
and DOD ≤ 30%

## Slide 29
Discharge power calculation
Power balance analysis
Discharge power in umbra including long-term and short-term loads
Discharge power in sunlight period when PSA< Pload
Depth of Discharge
DOD = Q discharge/ Q battery capacity

## Slide 30
Power balance analysis
No. | Items | Parameters
1 | Long-term load | 70W
2 | Max umbra period | 34.8min
3 | Min light period | 62.65min
4 | power supplied by solar array | 151W
5 | Battery discharge voltage | 3.60V
6 | Battery charge voltage | 4.10V
7 | Battery Series number | 7
8 | Battery capability (total) | 10Ah
9 | Discharge line loss factor | 97%
10 | Charge/discharge ratio | 1.01
Parameters for power balance analysis
Power budget
Sunlight and orbit condition
SA output power(EOL)
Various efficiencies
Parameters about battery

## Slide 31
Concept and Function
Compositions of PSS
Work principles of PSS
Telemetries and Tele-commands
Power balance analysis
OUTLINES

## Slide 32
Key Telemetry Parameters
According to the importance of different telemetries, transmission periods of TMs are still different.
Telemetries Type
Quick changing telemetries ( per 2 seconds )
Slow changing telemetries (per 16 seconds / 4 seconds )
There are 27 quick changing telemetries and 32 slow changing telemetries in PCDU.

## Slide 33
Quick changing telemetries in PCDU
# 28V Bus Voltage 23V～29V
# +12V Bus Voltage 10V～13V
# +5V Bus Voltage 4.5V～5.5V
# -12V Bus Voltage -10V～-14V
# Battery Voltage 23V～29V
# Load Current 0A～6A
# SA Output Current 0A～7A
# Charge Current 0A～5A
# Discharge Current 0A～6A
# Battery temperature 1 0oC～35oC
Key Telemetry Parameters
# Discharge Relay Status 0：ON，1：OFF
# -Y Wing Deployment Status
1：Deployed，0：Folded
# +Y Wing Deployment Status
1：Deployed，0：Folded
# Battery Heater Status 0：ON，1：OFF
# Over-discharge Flag
0：Normal，1：Over-discharge
# BMU Status 0：OFF，1：ON

## Slide 34
Key Telemetry Parameters
Slow changing telemetries in PCDU
# Battery current capacity
# Battery charge capacity
# Battery discharge capacity
# Power Alarm Status
# Sub Computer Selfcheck Status
# Sub-computer Status
# Heater Stop Temperature/ Heater start temperature
# Charge/Discharge Ratio
# Batt Voltage Alarm Threshold
# Batt Voltage Pre-alarm Threshold

## Slide 35
Key Tele-commands
OBDH _M ON
OBDH _B ON
Batt_Discharge_Relay_CLOSE
Batt_Discharge_Relay_OPEN
Overdischarge_s/w_ENABLE
Overdischarge_s/w_DISABLE
Batt_Connect_s/w_ENABLE
Batt_Connect_s/w_DISABLE
Transponder A_ON
Transponder A_OFF
Transponder B_ON
Transponder B_OFF

## Slide 36
Data blocks for PCDU
Charge parameters block
Bit | Data | Annotation
0 | ##H | 55H : data block
1 | ##H | 01H: charge parameters block
2 | ##H | Charge/Discharge Ratio
3 | ##H | Battery Current Capacity
4 | ##H | Battery Voltage Alarm Threshold
5 | ##H | Battery Voltage Discharge Alarm Threshold
6 | ##H | Battery Voltage Pre-alarm Threshold
7 | ##H | Battery Capacity Alarm Threshold
8 | ##H | AAH
If the injection parameter is 00H, the parameter will keep as it was without changing.
Charge parameters block

## Slide 37
Data blocks for PCDU
Heater control block
Bit | Data | Annotation
0 | ##H | 55H : data block;
1 | ##H | 02H: heaters control parameters block
2 | ##H | Temperature control mode D7D6：01-closed loop，10-open loop D5： 1- Heater start when open loop 0- Heater stop when open loop
3 | ##H | Heater stop temperature
4 | ##H | Heater start temperature
5 | ##H | AAH
6 | ##H | AAH
7 | ##H | AAH
8 | ##H | AAH

## Slide 38
Key Telemetry Parameters in BMU
# Battery Voltage
# Batt_Cell 1 Voltage
# Batt_Cell 2 Voltage
# Batt_Cell 3 Voltage
# Batt_Cell 4 Voltage
# Batt_Cell 5 Voltage
# Batt_Cell 6 Voltage
# Batt _Cell 7 Voltage
# Batt_Cell1_Bal_Status
# Batt_Cell2_Bal_Status
# Batt_Cell3_Bal_Status
# Batt_Cell4_Bal_Status
# Batt_Cell5_Bal_Status
# Batt_Cell6_Bal_Status
# Batt_Cell7_Bal_Status
# Batt_Bal_s/w Status

## Slide 39
Thanks!