## Slide 1: TT&C Subsystem In-Orbit Operation instructions
DFH SATELLITE CO., LTD.
Oct, 2019

## Slide 2: Content
Operation Overview
TC and Telemetry
In-orbit configuration
Constrains
Manual Procedure
Composition and function

## Slide 3: 1 Composition and function of TT&C
2 USB transponders, 2 GPS receivers, 2 S band antennas, 1 S band hybrid, 2 GPS antennas.

## Slide 4: 1 Composition and function of TT&C
Transponder
To transmit telemetry.
GPS receiver
Output position and orbit determination messages.
Antenna
The TT&C antenna receives or transmits the TT&C signal.
The GPS antenna receives signals from the GPS navigation satellites.
To receive and demodulate the uplink signals and output PCM signal to OBDH.
Broadcast the PPS signal which synchronizes satellite time.
The Multiplexer blends or distributes the TT&C signal.
Broadcast UTC time.

## Slide 5: Content
Operation Overview
TC and Telemetry
In-orbit configuration
Constrains
Manual Procedure
Composition and function

## Slide 6: 2 Operation Overview
The routine operation of TT&C system together with GCS during long-term management phase including telemetry, telecommand, tracking, and orbit maintenance.
At normal situation, two receivers of transponder work at the same time. The transmitter of transponder and GPS receiver operate on main module.
ETRSS-1 TT&C subsystem of satellite is not allowed to be operated by command in long-term management phase except emergency of TT&C subsystem.
Any abnormal situation or any switch from main module to standby module should be monitored and reported DFH immediately.

## Slide 7: Content
Operation Overview
TC and Telemetry
In-orbit configuration
Constrains
Manual Procedure
Composition and function

## Slide 8
3 Telecommands and Telemetry
3.1 Telecommands Of S Band Transponder
  All of the transponder’s commands are OC TC, the S band transponders commands are shown in the table.
  The commands listed in the table can be used to switch on or off the transponder’s transmitter. (Direct TC and indirect TC)
  Switch on transmitter B before Switch off transmitter A.
No. | TC Number | TC Name | Application & Description
1 | K13（KCB010） | Transmitter of USB B off | TB001（USB B transmitter on/off status）=0（off）
2 | K10（KCA009） | Transmitter of USB A on | TA001（USB A transmitter on/off status）=1（on）
3 | K11（KCB009） | Transmitter of USB B on | TB001（USB B transmitter on/off status）=1（on）
4 | K12（KCA010） | Transmitter of USB A off | TA001（USB A transmitter on/off status）=0（off）
Notes: F0: Fixed format telemetry

## Slide 9
3 Tele-commands and Telemetry
3.1 Telecommands Of S Band Transponder
  The commands listed in the table can be used to control the transponder’s coherent and ranging status . (Direct TC)
No. | TC Number | TC Name | Application & Description
1 | K14 | Transponder A and B coherent in work | TA005=1(A coherent in work) TB005=1 (B coherent in work)
2 | K15 | Transponder A and B incoherent in work | TA005=0 (A incoherent in work) TB005=0 (B incoherent in work)
3 | K16 | Transponder A and B ranging on | TA006=1 (A ranging on) TB006=1( B ranging on)
4 | K17 | Transponder A and B ranging off | TA006=0 (A ranging off) TB006=0( B ranging off)

## Slide 10
3.2 Telecommands Of GPS Receiver
  The GPS receiver’s commands are shown in the table.
  The 3 indirect OC commands can switch on or off the GPS receiver A and B.
  It’s forbidden that both the two GPS receivers are switch on at the same time.
No. | TC Number | TC Name | Application & Description
1 | KSM112-07 | GPS Receiver A on | GS004 (GPS receiver A/B status)=0(A) NS006(Load current) increase 0.8~1A
2 | KNY03003 | GPS Receiver B on | GS004 (GPS receiver A/B status)=1(B) NS006(Load current) increase 0.8~1A
3 | KSM112-08 | GPS Receiver A and B off | NS006(Load current) decrease 0.8~1A
3 Tele-commands and Telemetry

## Slide 11
3.2 Telecommands Of GPS Receiver
  The two GPS receivers have the same CAN bus communication format, the two GPS receivers share a series of data command (Total 16 data commands).
  The 4 commands shown in the table can reset the GPS receiver, navigation orientation software, CAN A bus and CAN B bus of GPS receiver.
No. | TC Number | TC Name | Application & Description
1 | KGS001 | GPS receiver resetting | GH001 (counter of TIC): increase from 0
2 | KGS002 | Navigation orientation software resetting | GH135(counter of tributary core resetting):plus 1 GH136(reason of tributary core resetting):0001
3 | KGS015 | CAN A bus resetting | GH130(counter of CAN A resetting ): plus 1 GH129(reason of CAN A resetting ): 0x5
4 | KGS016 | CAN B bus resetting | GH132(counter of CAN B resetting ): plus 1 GH131(reason of CAN B resetting ): 0x5
3 Tele-commands and Telemetry

## Slide 12
3.2 Telecommands Of GPS Receiver
  The other 12 Data commands usually not allowed to be send, as follows:
No. | TC Number | TC purpose
1 | KGS003 | navigation orientation software upload permission
2 | KGS004 | navigation orientation software upload ending
3 | KGS005 | navigation orientation software upload startup
4 | KGS006 | orbit determination software upload permission
5 | KGS007 | orbit determination software upload ending
6 | KGS008 | orbit determination software upload startup
7 | KGS009 | Allowing 1pps output
8 | KGS010 | Forbidding 1pps output
9 | KGS011 | time broadcast at CAN bus A
10 | KGS012 | time broadcast at CAN bus B
11 | KGS013 | orbit determination data output permission
12 | KGS014 | orbit determination data output forbidden
3 Tele-commands and Telemetry
Notes: 1PPS output control strategy:
Controlled by GPS positioning status (default): sending 1PPS on positioning status, otherwise not output pulse.
Controlled by commands: There are two commands: 1PPS Output Allow and Forbid 1PPS Output.1PPS and broadcasting data of time only controlled by the commands, and have nothing with positioning status until the GPS receiver being reset.

## Slide 13
TM Name | Data length (bytes) | Number of TM | Collection Period (second)
Transponder A | 16 | 32 | 1s
Transponder B | 16 | 32 | 1s
GPS fast TM | 20 | 15 | 2s
GPS status slow | 128 | 160 | 32s
GPS orbit slow | 87 | 29 | 32s
3.3 Telemetry Parameters of TT&C
  Brief introduction of TM

## Slide 14
3.3 Telemetry Parameters of TT&C
  The telemetry is shown in OBDH’s Temperature packet (1P/32s)
TM Number | TM Name | Data Type | Unit | Normal Value
XE017 | TMP of stack(beside transponder and GPS receiver ) | TH | ℃ | -15～50℃
TM Number | TM Name | Data Type | Unit | Normal Value
TA021 | TMP of Transponder A | TH | ℃ | -15～55℃
TB021 | TMP of Transponder B | TH | ℃ | -15～55℃
  The temperature telemetry is shown in Transponder ’s packet (1P/1s)

## Slide 15
3.3.1 Telemetry Parameters of Transponder
  Parts of transponder telemetry parameters which are also shown in in fixed telemetry.
TM Number | TM Name | Data Type | Unit | Description & Processing
TA001(TB001) | Transmitter A(B) on/off status | BL | — | 1: On, 0: Off
TA002(TB002) | Carrier lock status of transponder A(B) | BL | — | 1: Lock, 0: Unlock
TA005(TB005) | Coherent status of transponder A(B) | BL | — | 1: Coherent, 0: Non-coherent
TA006(TB006) | Ranging status of transponder A(B) | BL | — | 1: On, 0: Off
TA013(TB013) | F(S) of transponder A(B) | DS | kHz | -128～127
TA014(TB014) | SNR voltage of transponder A(B) | DS | / | 70~110
TA016(TB016) | Transponder A(B) transmitter power | AN | V | 2.5～3.5

## Slide 16
3.3.2 Telemetry Parameters of GPS Receiver
Parts of GPS Receiver’s Fast Telemetry :1P/2s
No. | TM Number | TM Name | Data Type | Description & Processing
1 | GS003 | Available navigation satellites number | DS | Available navigation star
2 | GS004 | GPS A/B mark | BL | 0：GPS A on duty ； 1：GPS B on duty ；
3 | GS005 | Positioning state | BL | 1：Positioning state； 0：Non-positioning state
4 | GS006 | Orbit determination state | BL | 00b：Invalidation； 01b：Invalidation； 10b：Extrapolating； 11b：Orbit determination
5 | GS012 | highest S/N mark | BL | 000:<30dB; 001:30～40dB; 010:40～50dB; 011:>50dB

## Slide 17
Parts of GPS Receiver’s Status Slowly Changing Telemetry :1P/32s
No. | TM Number | TM Name | Description & Processing
1 | GH008 | Orbit determination data output marking | 11b:permission; 10b:forbidden;
2 | GH009 | 1pps output marking | 11b:permission; 10b: forbidden; 00b: initial(permission)
3 | GH154 | Orbit determination PDOP value | 0～255
5 | GH130 | Bus A reset counter | 0~15
6 | GH132 | Bus B reset counter | 0~15
7 | GH135 | Counter of tributary core resetting | 0~15
3.3.2 Telemetry Parameters of GPS Receiver

## Slide 18
GPS Receiver’s Orbit Slowly Changing Telemetry : 1/8s
3.3.2 Telemetry Parameters of GPS Receiver
NO | TM Number | TM Name | Description & Processing
1 | GA001 | Absolute positioning time | Fill with AAH before positioning.
2 | GA002 | X1 | (WGS-84) Satellite position X1
3 | GA003 | Y1 | (WGS-84) Satellite position Y1
4 | GA004 | Z1 | (WGS-84) Satellite position Z1
5 | GA005 | Vx1 | (WGS-84) Satellite speed Vx1
6 | GA006 | Vy1 | (WGS-84) Satellite speed Vy1
7 | GA007 | Vz1 | (WGS-84) Satellite speed Vz1
8 | GA008 | Absolute positioning data available | 0XAA: Available; 0X55: Unavailable
9 | GA010 | Orbit determination filter state | 011b: orbit determination filter state 110b: orbit extrapolating state

## Slide 19
3.3.2 Telemetry Parameters of GPS Receiver
NO | TM Number | TM Name | Description & Processing
10 | GA016 | Orbit determination time | Fill with AAH before positioning or in state of rest
11 | GA017 | X2 | (WGS-84) Satellite position X2
12 | GA018 | Y2 | (WGS-84) Satellite position Y2
13 | GA019 | Z2 | (WGS-84) Satellite position Z2
14 | GA020 | Vx2 | (WGS-84) Satellite speed Vx2
15 | GA021 | Vy2 | (WGS-84) Satellite speed Vy2
16 | GA022 | Vz2 | (WGS-84) Satellite speed Vz2
17 | GA023 | （a）(root semi major axis) | (J2000, instantaneous root)
18 | GA024 | （e）(eccentricity) | (J2000, instantaneous root)
19 | GA025 | （i）(inclination) | (J2000, instantaneous root)
20 | GA026 | （Ω）(longitude of ascending node) | (J2000, instantaneous root)
21 | GA027 | （ω）(argument of perigee) | (J2000, instantaneous root)
22 | GA028 | （M）(mean anomaly) | (J2000, instantaneous root)

## Slide 20: Content
Operation Overview
TC and Telemetry
In-orbit configuration
Constrains
Manual Procedure
Composition and function

## Slide 21: 4 In-orbit configuration
The configuration is for the regular mission of long-time management.
Two receivers of transponder are switching on; the transmitter A is switching on, the transmitter B is switching off.
Transponders are in coherent and ranging off state.
GPS receiver A is switching on and positioning stable.

## Slide 22
No. | Unit | Status | TM number | TM content
1 | Transponder | Receiver：Hot backup | TA014 | SNR of transponder A :70~110
 |  |  | TB014 | SNR of transponder B :70~110
2 |  |  | TA002 | Transponder Lock of carrier A: 1
 |  |  | TB002 | Transponder Lock of carrier B: 1
3 |  | Transmitter ：A work | TA001 | Transponder transmitter A on/off : 1
 |  |  | TB001 | Transponder transmitter B on/off : 0
4 |  |  | TA016 | Transmitter A output power : 2.5～3.5V
 |  |  | TB016 | Transmitter B output power: 0V
5 |  | Transponder A and B coherent in work | TA005 | transponder A coherent/incoherent: 1
 |  |  | TB005 | transponder B coherent/incoherent: 1
 |  | Transponder A and B Ranging on | TA006 | transponder A Ranging on/off : 0
6 |  |  |  | 
 |  |  | TB006 | transponder A Ranging on/off : 0
4.1 TM and Status of Transponder During Long Term Management

## Slide 23
No. | Unit | Status | TM number | TM content
1 | GPS Receiver | GPS receiver A work | GS004 | GPS A/B mark: 0
2 |  | positioning state | GS005 | positioning state: 1
 |  | orbit determination state | GS006 | orbit determination state:11
5 |  | UTC time | GS001 | UTC time: second accumulated continuous from 2009/1/1 00:00:00)
4.2 TM and Status of GPS Receiver During Long Term Management

## Slide 24: Content
Operation Overview
TC and Telemetry
In-orbit configuration
Constrains
Manual Procedure
Composition and function

## Slide 25: 5 Constrains
The general constrains for GCS：
Telemetry, Telecommand and tracking should be only be conducted after the satellite and TT&C ground station captured each other .
TT&C ground station should control the output power to make sure the input power level of the transponder is less than -50dBm and more than sensitive level. It’s forbidden to add the uplink signal power arbitrarily to avoid destroying the receiver of transponder.
Normally, the ground station could stop sweeping the uplink carrier when both the 2 transponders are in lock status.
To avoid the transponder false locking the TC subcarrier, the TC subcarrier should be in idle on status(subcarrier be modulated on carrier only when sending commands).

## Slide 26
S Band Transponder Constrains
  The transponder’s default status is coherent and ranging off, the commands of coherent off and ranging on are forbidden without the satellite manufacturer participating.
  Switch off the transmitter or changing the transmitter is forbidden.
  When the main transmitter failed, the transmitter should be switch to backup transmitter on condition that getting authorization form DFH. It’s required that firstly switch on the backup transmitter then switch off the failure transmitter.
  It’s better to avoid the two transmitters work at the same time when satellite is out of the ground station’s control.

## Slide 27
GPS Receiver Constrains
  It is forbidden that two GPS receivers work at the same time. Because two GPS receivers have the same CAN bus communication address, so the CAN bus communication would be confused.
  Checking the telemetry of receiver to make sure which GPS receivers is switching on.
No. | status | TM Name | Data Type | UTM number | Normal Value
1 | A on B off | GPS receiver A/B status | BL | GS004 | 0
2 | B on A off | GPS receiver A/B status | BL | GS004 | 1

## Slide 28: Content
Operation Overview
TC and Telemetry
In-orbit configuration
Constrains
Manual Procedure
Composition and function

## Slide 29: 6 Manual Procedure
TT&C subsystem perform tracking and capturing the satellite, if the telemetry of TT&C is in normal range, no operation should be done.
If there any telemetry of TT&C is out of the normal range , must take measures according to the situation and ask for engineering support.
The Manual Procedure of ETRSS-1 is given in Table, which specifies the major function and operation procedure of TT&C subsystem during abnormal situation together with GCS.

## Slide 30
No | Failure Mode | Reason | Failure Analysis | Failure Detection | Measures | Action
 | No Telemetry | Transmitter Fails | There is no telemetry and could not schedule new missions. | If there is no downlink carrier, transmitter probably fails | If transmitter A is work To execute the procedure: A-1 To switch transmitter A To transmitter B | Take measures immediately then inform DFH
 |  |  |  |  | If transmitter B is work To execute the procedure: A-2 To switch transmitter B To transmitter A | 
Transponder Failure Mode Operations

## Slide 31
No | Failure Mode | Reason | Failure Analysis | Failure Detection | Measures | Action
2 | Transponder coherence module fails | There is a problem with the coherent function of the transponder | The ranging function of the transponder is not working. | 1)Transponder A coherent/incoherent = 0:incoherence 2)Transponder B coherent/incoherent = 0:incoherence If either of the above two cases last more than 10 seconds, the failure can be detected. | If transmitter A is work To execute the procedure: A-3 To Enable Coherent Mode of Transponder if failure still exist, to execute the following procedures: A-1 To switch transmitter A To transmitter B, A-3 To Enable Coherent Mode of Transponder | Ask for authorization to DFH before take measures
 |  |  |  |  | If transmitter B is work To execute the procedure: A-3 To Enable Coherent Mode of Transponder if failure still exist, to execute the following procedures: A-2 To switch transmitter B To transmitter A, A-3 To Enable Coherent Mode of Transponder | 
Transponder Failure Mode Operations

## Slide 32: GPS Failure Mode Operations
No | Failure Mode | Reason | Failure Analysis | Failure Detection | Measures | Action
3 | GPS can’t accomplish positioning for long time. | GPS tributary core fails | GPS can’t provide positioning data even after autonomic reset | Positioning state =‘0’ invalid Positioning module TIC counter 1)The fault lasts more than 30 seconds and the fault could not be recovered by the autonomic reset. (TIC value in this orbit is smaller than its value of last orbit the operator shall take measures in current orbit;) 2) The fault lasts less than 30 seconds (TIC value in this orbit is larger than its value in last orbit and TIC is continuous, the operator can choose to take measures in next orbit for further observation.) | 1)If GPS A is on duty, to execute the following procedure: B-3 To reset navigation positioning software B-2 To reset GPS receiver If the failure continues to execute: B-1 Switch GPS receiver A to GPS receiver B 2)If GPS B is on duty, to execute the following procedure: B-3 To reset navigation positioning software B-2 To reset GPS receiver If the failure continues, to execute: B-2 Switch GPS receiver B to GPS receiver A | Take measures in current orbit or in next orbit then inform DFH

## Slide 33
No | Failure Mode | Reason | Failure Analysis | Failure Detection | Measures | Action
4 | GPS UTC Time failure | GPS receiver does not position | Satellite loses highly accurate time system | UTC time=“0’’ or doesn’t update | 1)If GPS A is on duty, to execute the following procedure: B-3 To reset GPS receiver A If the failure continues to execute: B-1 Switch GPS receiver A to GPS receiver B 2)If GPS B is on duty, to execute the following procedure: B-4 To reset GPS receiver B If the failure continues to execute: B-2 Switch GPS receiver B to GPS receiver A | Take measures in current orbit or in next orbit then inform DFH
 |  | UTC time is abnormally changed by space electric particle |  |  |  | 

## Slide 34
No | Failure Mode | Reason | Failure Analysis | Failure Detection | Measures | Action
5 | GPS receiver doesn’t output orbit determination data | GPS receiver main core fails | GPS receiver main core data is abnormal | Positioning state =1:positioning data orbit determination state=00: invalid; If the above case lasts more than 30 seconds, the failure can be detected | 1)If GPS A is on duty, to execute the following procedure: B-3 To reset GPS receiver If the failure continues, to execute: B-1 Switch GPS receiver A to GPS receiver B 2)If GPS B is on duty, to execute the following procedure: B-3 To reset GPS receiver If the failure continues, to execute: B-2 Switch GPS receiver B to GPS receiver A | Take measures in current orbit then inform DFH
 |  |  |  | Positioning state =1：positioning data orbit determination state=11,“orbit determination” X2~Vz2 output data error or invalid data AA If the above case lasts more than 30 seconds, the failure can be detected |  | 

## Slide 35
No | Failure Mode | Reason | Failure Analysis | Failure Detection | Measures | Action
6 | Communication error between GPS receiver and OBDH. | GPS CAN-bus fault or GPS sub-computer fault | GPS TM packet is abnormal and can’t monitor the GPS status | GPS TM packet is filled by EE or there is no change for data in TM packet; The TM ‘GPS TM invalidation counter’ increases abnormally | 1)If GPS A is on duty, to execute the following procedure: B-4 “To reset CAN bus A controller If the failure continues, to execute: B-3 To reset GPS receiver If the failure continues, to execute: B-1 Switch GPS receiver A to GPS receiver B 2)If GPS B is on duty, to execute the following procedure: B-5 “To reset CAN bus B controller If the failure continues, to execute: B-3 To reset GPS receiver If the failure continues, to execute: B-2 Switch GPS receiver B to GPS receiver A | Ask for authorization to DFH before take measures

## Slide 36: Appendix A
No | TM before sending | TC Number | TC Name | TM after sending
1 | TA001 Transponder transmitter A on/off: 1=ON TB001 Transponder transmitter B on/off: 0=OFF | K11 (Direct TC) or KCB009 (Indirect TC) | Transmitter B of USB transponder on (to send it 3 times) | TA001 Transponder transmitter A on/off: 1=ON TB001 Transponder transmitter B on/off: 1=ON
2 | TA001 Transponder transmitter A on/off: 1=ON TB001 Transponder transmitter B on/off: 1=ON | K12 (Direct TC) or KCA010 (Indirect TC) | Transmitter A of USB transponder off (to send it 3 times) | TA001 Transponder transmitter A on/off: 1=OFF TB001 Transponder transmitter B on/off: 1=ON
Table A‑1 Steps of switch Transmitter A to Transmitter B

## Slide 37: Appendix A
No | TM before sending | TC Number | TC Name | TM after sending
1 | TA001 Transponder transmitter A on/off: 1=OFF TB001 Transponder transmitter B on/off: 1=ON | K10 (Direct TC) or KCA009 (Indirect TC) | Transmitter A of USB transponder on (to send it 3 times) | TA001 Transponder transmitter A on/off: 1=ON TB001 Transponder transmitter B on/off: 1=ON
2 | TA001 Transponder transmitter A on/off: 1=ON TB001 Transponder transmitter B on/off: 1=ON | K13 (Direct TC) or KCB010 (Indirect TC) | Transmitter B of USB transponder off (to send it 3 times) | TA001 Transponder transmitter A on/off: 1=ON TB001 Transponder transmitter B on/off: 1=OFF
Table A‑2 Steps of switch Transmitter B to Transmitter A

## Slide 38: Appendix A
TM before sending | TC Number | TC Name | TM after sending
TA005 transponder A coherent/incoherent: 0=incoherent TB005 transponder B coherent/incoherent 0=incoherent | K14 (Direct TC) KCA011 (Indirect TC) KCB011 (Indirect TC) | USB transponder (A and B) coherent USB transponder A coherent USB transponder B coherent | TA005 transponder A coherent/incoherent: 1=coherent TB005 transponder B coherent/incoherent 1=coherent
Table A‑3 Telecommand for changing from Incoherent to Coherent Mode

## Slide 39: Appendix B
Table B‑1 Switch GPS receiver A to GPS receiver B
No | TM before sending | TC Number | TC Name | TM after sending
1 | GS004 Receiver A/B: 0=A NS006 Load current | KSM112-08 (Indirect OC TC) | GPS receiver A and B Off | GS004 Receiver A/B: 0=A NS006 Load current decrease 0.8~1A
2 | GS004 Receiver A/B: 0=A NS006 Load current | KNY03003 (Indirect OC TC) | GPS receiver B ON | GS004 Receiver A/B: 1=B NS006 Load current increase 0.8~1A

## Slide 40: Appendix B
No | TM before sending | TC Number | TC Name | TM after sending
1 | GS004 Receiver A/B: 1=B NS006 Load current | KSM112-08 (Indirect OC TC) | GPS receiver A and B Off | GS004 Receiver A/B: 1=B NS006 Load current decrease 0.8~1A
2 | GS004 Receiver A/B: 1=B NS006 Load current | KSM112-07 (Indirect OC TC) | GPS receiver A ON | GS004 Receiver A/B: 0=A NS006 Load current increase 0.8~1A
Table B‑2 Switch GPS receiver B to GPS receiver A

## Slide 41: Appendix B
No | TM before sending | TC Number | TC Name | TM after sending
1 | GH001 counter of TIC | KGS001 (Indirect OC TC) | GPS receiver resetting | GH001 counter of TIC: increase from 0
2 | NS006 Load current | KSM112-08 (Indirect OC TC) | GPS receiver A and B Off | NS006 Load current decrease 0.8~1A
 | NS006 Load current | KSM112-07 (Indirect OC TC) | GPS receiver A ON | NS006 Load current increase 0.8~1A
Table B‑3 Steps for reset GPS receiver A

## Slide 42: Appendix B
No | TM before sending | TC Number | TC Name | TM after sending
1 | GH001 counter of TIC | KGS001 (Indirect OC TC) | GPS receiver resetting | GH001 counter of TIC: increase from 0
2 | NS006 Load current | KSM112-08 (Indirect OC TC) | GPS receiver A and B Off | NS006 Load current decrease 0.8~1A
3 | NS006 Load current | KNY03003 (Indirect OC TC) | GPS receiver B ON | NS006 Load current increase 0.8~1A
Table B‑4 Steps for reset GPS receiver B

## Slide 43: Appendix B
No | TM before sending | TC Number | TC Name | TM after sending
1 | GH130 CAN bus A reset count GH129 CAN bus A last reset reason | KGS015 | GPS receiver CAN bus A reset | GH130 CAN bus A reset count plus 1 GH129 CAN bus A last reset reason: 0x5=receive CAN bus A reset command
Table B‑6 Telecommands for reset CAN bus B of GPS receiver
Table B‑5 Telecommands for reset CAN bus A of GPS receiver
No | TM before sending | TC Number | TC Name | TM after sending
1 | GH132 CAN bus B reset count GH131 CAN bus B last reset reason | KGS016 | GPS receiver CAN bus B reset | GH132 CAN bus B reset count plus 1 GH131 CAN bus B last reset reason: 0x5=receive CAN bus B reset command

## Slide 44: Appendix C
AGC variation with temperature of Transponder A

## Slide 45: Appendix C
AGC variation with temperature of Transponder B

## Slide 46: Appendix C
SNR variation with temperature of Transponder A

## Slide 47: Appendix C
SNR variation with temperature of Transponder B

## Slide 48: Appendix C
Power telemetry variation with temperature

## Slide 49
Thank you