## Slide 1: ETRSS-1 DTS In orbit operation instructions
DFH SATELLITE CO., LTD.
Oct, 2019

## Slide 2: CONTENTS
1
Composition and function of DTS in orbit
2
Working mode of DTS in orbit
3
Telecommand and telemetry of DTS
4
Sequence of operation
5
Important Notice
6
The Anomaly Operation in orbit

## Slide 3: 1 Composition and function of DTS
Data Transmission Subsystem is an important subsystem of ETRSS-1 satellite. It receives and processes data from camera, then transmitting the data to ground station. The transmission mate is up to 100Mbps.
The DTS is composed of the three parts: DTS integrated transmission machine, phased-array antenna and coaxial cable.

## Slide 4: 1 Composition and function of DTS
No | Device Name | Device Number | Quantity of FM (piece/set)
1 | Integrated transmission machine | ETRSSA01-1 | 1
2 | Phased-array antenna | ETRSSA02-1 | 1
3 | Coaxial cable | ETRSSA03-1 | 1
Integrated transmission machine: including base band processing segment, RF processing segment and power source segment;
Phased-array antenna: receiving signal form integrated transmission machine and transmitting to ground system;
Coaxial cable: the channel to transfer the RF signal from integrated transmission machine to phased-array antenna.

## Slide 5
DTS Block Diagram
1 Composition and function of DTS

## Slide 6: 1 Composition and function of DTS
The functions of DTS are described as following:
DTS has the function of compressing the data of the Multi-spectrum Camera, collecting the compressed MSC data and transferring them to the GS.
DTS also possesses the functions of data formatting, data recording, modulating, and data transmission.
SSM has the function of erasing all, sequential record, sequential replay, recording by file address and replay by address.

## Slide 7: CONTENTS
1
Composition and status of DTS in orbit
2
Working mode of DTS in orbit
3
Telecommand and telemetry of DTS
4
Sequence of operation
5
Important Notice
6
The Anomaly Operation in orbit

## Slide 8: 2 working mode of DTS in orbit
There are three working modes:
Record mode
When the satellite is not being accessible to GS, DTS receives the real-time data of cameras, after digital signal processing, SSM records the processed data.
replay mode
When the satellite is accessible to GS, DTS transmits the data recorded in storage device to the ground station after digital signal processing, modulating and amplifying.
Real-time mode
When the satellite is accessible to ground station, MSC are imaging and DTS receives the data of cameras. After digital signal processing, modulating, amplifying, DTS sends RF signals to ground station in real-time .

## Slide 9: 2 working mode of DTS in orbit
Considering backup of SSM, ratio of compression, record and play by sequence or address, there are 9 kinds of working combined mode.
mode | Main SSM | Backup SSM | 2:1 compression | Lossless compression | Record and replay by sequence | Record and replay by address
Record and replay | √ | × | √ | × | √ | ×
 | √ | × | √ | × | × | √
 | √ | × | × | √ | √ | ×
 | √ | × | × | √ | × | √
 | × | √ | √ | × | √ | ×
 | × | √ | √ | × | × | √
 | × | √ | × | √ | √ | ×
 | × | √ | × | √ | × | √
Real-time | / | / | √ | × | / | /

## Slide 10: CONTENTS
1
Composition and status of DTS in orbit
2
Working mode of DTS in orbit
3
Telecommand and telemetry of DTS
4
Sequence of operation
5
Important Notice
6
The Anomaly Operation in orbit

## Slide 11: 3 Telecommand and telemetry of DTS
3.1 There are three kinds of telecommand：
Telecommand type | OC telecommand | Data telecommand | Data block
Telecommand number | 2 | 35 | 4

## Slide 12: 3 Telecommand and telemetry of DTS
3.1.1 DTS OC tele command
NO | TC Number | TC name | Application & Description
1 | KSM112-19 | DTS turn on | NS006 Load current increase 0.2~0.25A; TMYA002 FPGA Load state: 1=Load success
2 | KSM112-1A | DTS turn off | NS006 Load current decrease 0.2~0.25A;

## Slide 13: 3 Telecommand and telemetry of DTS
3.1.2 DTS data telecommand
NO | TC Number | TC name | Application & Description
1 | KYA001 | Modulation mode | TMYA005 RF modulation state: 0=Modulation state
2 | KYA002 | Carrier mode | TMYA005 RF modulation state: 1=Carrier state
3 | KYA003 | RF and antenna turn on | TMYA003 RF and antenna state: 1= RF and antenna turned on
4 | KYA004 | RF and antenna turn off | TMYA003 RF and antenna state: 1= RF and antenna turned off
5 | KYA005 | Real-time transmit on | TMYA004 Real-time transmit state:0=real-time transmit on

## Slide 14: 3 Telecommand and telemetry of DTS
3.1.2 DTS data telecommand
NO | TC Number | TC name | Application & Description
6 | KYA006 | Real-time transmit off | TMYA004 Real-time transmit state:0=real-time transmit off
7 | KYA007 | Lossless compression | TMYA008 Compression state: 1=lossless compression
8 | KYA008 | 2:1 compression | TMYA008 Compression state: 1=2:1 compression
9 | KYA009 | main SSM working | TMYA010 SSM backup state: 0000=main SSM in use
10 | KYA010 | spare SSM working | TMYA010 SSM backup state: 0000=spare SSM in use

## Slide 15: 3 Telecommand and telemetry of DTS
3.1.2 DTS data telecommand
NO | TC Number | TC name | Application & Description
11 | KYA011 | SSM pointer saving | TMYA017 Pointer saving counter: plus 1
12 | KYA012 | SSM pointer restoring | TMYA018 Pointer restoring counter: plus 1
13 | KYA013 | SSM recoding by sequence | TMYA011 SSM working state: 0110=SSM recoding by sequence
14 | KYA014 | SSM recoding by address | TMYA011 SSM working state: 1001=SSM recoding by address
15 | KYA015 | SSM recording stop | TMYA011 SSM working state: 0111=SSM recording over

## Slide 16: 3 Telecommand and telemetry of DTS
3.1.2 DTS data telecommand
NO | TC Number | TC name | Application & Description
16 | KYA016 | SSM replaying by sequence | TMYA011 SSM working state: 1000=SSM replaying by sequence
17 | KYA017 | SSM replaying by address | TMYA011 SSM working state: 1010=SSM replaying by address
18 | KYA018 | SSM replaying stop | TMYA011 SSM working state: 1011=SSM replaying over
19 | KYA019 | SSM resetting | TMYA029 SSM replaying address: 0000H
20 | KYA020 | SSM self detecting | TMYA011 SSM working state: 0001=be self detecting, after about 5 minutes, 1100= self detecting over

## Slide 17: 3 Telecommand and telemetry of DTS
3.1.2 DTS data telecommand
NO | TC Number | TC name | Application & Description
21 | KYA021 | SSM erasing | TMYA011 SSM working state: 0010=be erasing, after about 4 minutes, 0011= erasing over
22 | KYA022 | Antenna calculation mode on | TMYA037 Antenna working mode: 01= calculation mode
23 | KYA023 | Antenna calculation mode off | TMYA037 Antenna working mode: 00=idle mode
24 | KYA024 | Antenna injection Pointing mode on | TMYA037 Antenna working mode: 10=injection pointing mode
25 | KYA025 | Antenna injection Pointing mode off | TMYA037 Antenna working mode: 00=idle mode

## Slide 18: 3 Telecommand and telemetry of DTS
3.1.2 DTS data telecommand
NO | TC Number | TC name | Application & Description
26 | KYA026 | Switch to GS 1 | TMYA038 Ground station marking: GS 1
27 | KYA027 | Switch to GS 2 | TMYA038 Ground station marking: GS 2
28 | KYA028 | Switch to GS 3 | TMYA038 Ground station marking: GS 3
29 | KYA029 | Switch to GS 4 | TMYA038 Ground station marking: GS 4
30 | KYA030 | Switch to GS 5 | TMYA038 Ground station marking: GS 5

## Slide 19: 3 Telecommand and telemetry of DTS
3.1.2 DTS data telecommand
NO | TC Number | TC name | Application & Description
31 | KYA031 | Switch to GS 6 | TMYA038 Ground station marking: GS 6
32 | KYA032 | Switch to GS 7 | TMYA038 Ground station marking: GS 7
33 | KYA033 | Switch to GS 8 | TMYA038 Ground station marking: GS 8
34 | KYA034 | CAN A bus resetting | TMYA012 CAN A bus resetting counter: plus 1
35 | KYA035 | CAN B bus resetting | TMYA013 CAN B bus resetting counter: plus 1

## Slide 20: 3 Telecommand and telemetry of DTS
3.1.3 DTS data block— function
Block | Function & description
Block1:Recording address block | When the SSM is recording by address, the data block1 injected designating the starting recording address of SSM
Block2:Replaying address block | When the SSM is replaying by address, the data block2 injected designating the starting and ending replaying address of SSM
Block3:Pointing angle block | When the phased-array antenna is in injection pointing mode, the data block3 injected designating the pointing angle of antenna at a persistent time
Block4:Ground parameter block | The data block4 designating the longitude, altitude and lattitude of eight ground stations.

## Slide 21: 3 Telecommand and telemetry of DTS
There are two kinds of telemetry:
Telemetry type | Fast changing telemetry | Slowly changing telemetry
Telemetry number | 19 | 18
Period | 1P/2s | 1P/16s

## Slide 22: 3 Telecommand and telemetry of DTS
DTS fast changing telemetry
NO | TM Number | TM Name | Data Type | Unit | Description & Processing
1 | TMYA002 | FPGA Load state | BL | / | 1: Load success
2 | TMYA003 | RF and antenna state | BL | / | 1: RF and antenna turned on 0: RF and antenna turned off
3 | TMYA004 | Real-time transmit state | BL | / | 0: Real-time transmit on 1: Real-time transmit off
4 | TMYA005 | RF modulation state | BL | / | 0: Modulation state 1: Carrier state
5 | TMYA008 | Compression state | BL | / | 1: Lossless compression 0: 2:1 compression

## Slide 23: 3 Telecommand and telemetry of DTS
DTS fast changing telemetry
NO | TM Number | TM Name | Data Type | Unit | Description & Processing
6 | TMYA010 | SSM main/standby state | BL | / | 0000b: Main SSM in use 1111b: Standby SSM in use
7 | TMYA011 | SSM working state | BL | / | 0000b: SSM idle 0001b: Self detecting 0010b: SSM erasing 0011b: Erasing over 0100b: Be resetting 0101b: Resetting over 0110b: Recording by sequence 0111b: Recording over 1000b: Replaying by sequence 1001b: Recoding by address 1010b: Replaying by address 1011b: Replaying over 1100b: Self detecting over

## Slide 24: 3 Telecommand and telemetry of DTS
DTS fast changing telemetry
NO | TM Number | TM Name | Data Type | Unit | Description & Processing
8 | TMYA012 | CAN A bus resetting counter | DS | / | CAN A bus resetting counter(0~15)
9 | TMYA013 | CAN B bus resetting counter | DS | / | CAN B bus resetting counter(0~15)
10 | TMYA014 | CAN A bus command implementing counter | DS | / | CAN A bus command implementing counter(0~15)
11 | TMYA015 | CAN B bus command implementing counter | DS | / | CAN B bus command implementing counter(0~15)
12 | TMYA016 | SSM room state | BL | / | 0000b：Not empty and not full 0011b：Empty 1100b：Full

## Slide 25: 3 Telecommand and telemetry of DTS
DTS fast changing telemetry
NO | TM Number | TM Name | Data Type | Unit | Description & Processing
13 | TMYA017 | Pointer saving counter | DS | / | Pointer saving counter (0~3)
14 | TMYA018 | Pointer restoring counter | DS | / | Pointer restoring counter (0~3)
15 | TMYA019 | Receiving GPS broadcast counter | DS | / | Receiving GPS broadcast counter (0~15)
16 | TMYA020 | Transferring GPS broadcast counter | DS | / | Transferring GPS broadcast counter (0~15)
17 | TMYA021 | Receiving time on-board broadcast counter | DS | / | Receiving time on-board broadcast counter (0~15)

## Slide 26: 3 Telecommand and telemetry of DTS
DTS fast changing telemetry
NO | TM Number | TM Name | Data Type | Unit | Description & Processing
18 | TMYA022 | Transferring time on-board broadcast counter | DS | / | Transferring time on-board broadcast counter (0~15)
19 | RM006 | Antenna current | AN | A | The current change when antenna turned on

## Slide 27: 3 Telecommand and telemetry of DTS
DTS slowly changing telemetry
TM Number | TM Name | Data Type | Unit | Description & Processing
TMYA023 | SSM recording pointer | DS | / | Recording position of SSM (0~16383)
TMYA024 | Receiving attitude broadcast counter | DS | / | Receiving attitude broadcast counter (0~15)
TMYA025 | Transferring attitude broadcast counter | DS | / | Transferring attitude broadcast counter (0~15)
TMYA026 | GPS time availability sign | BL | / | 1: Available 0: Unavailable
TMYA027 | GPS positioning or orbit determination data | BL | / | 101b: Absolute positioning data 011b: Orbit determination data 110b: Orbit extrapolating data

## Slide 28: 3 Telecommand and telemetry of DTS
DTS slowly changing telemetry
TM Number | TM Name | Data Type | Unit | Description & Processing
TMYA028 | GPS data error counter | DS | / | GPS data error counter (0~15)
TMYA029 | SSM replaying pointer | DS | / | Replaying position of SSM (0~16383)
TMYA030 | Number of SSM effective block | DS | / | Number of SSM effective block (0~16383)
TMYA031 | Center angle of antenna | DS | 0.1° | center angle of antenna (0~360°)
TMYA032 | Azimuth angle of antenna | DS | 0.1° | Azimuth angle of antenna (0~360°)

## Slide 29: 3 Telecommand and telemetry of DTS
DTS slowly changing telemetry
TM Number | TM Name | Data Type | Unit | Description & Processing
TMYA033 | Counter of receiving telecommand | DS | / | 0~255
TMYA034 | Counter of executing telecommand | DS | / | 0~255
TMYA035 | Time synchronization state of antenna | BL | / | 0: Failure 1: Success
TMYA036 | Injecting pack state of antenna | BL | / | 0: Failure 1: Success
TMYA037 | Antenna working mode | BL | / | 01: Independent calculation mode 00: Idle mode 10: Injection Pointing mode

## Slide 30: 3 Telecommand and telemetry of DTS
DTS slowly changing telemetry
TM Number | TM Name | Data Type | Unit | Description & Processing
TMYA038 | Ground station marker | BL | / | 0001b：GS 1；0010b：GS 2：0011b：GS 3；0100b：GS 4；0101b：GS 5；0110b：GS 6；0111b：GS 7；1000b：GS 8
TMYA039 | Antenna inner time | DS | s | Lower 4 bits of inner second (0~15)
TMYA040 | Injecting pack serial number of antenna | DS | / | Lower 4 bits of injecting pack serial number (0~15)

## Slide 31: CONTENTS
1
Composition and status of DTS in orbit
2
Working mode of DTS in orbit
3
Telecommand and telemetry of DTS
4
Sequence of operation
5
Important Notice
6
The Anomaly Operation in orbit

## Slide 32: 4 Sequence of operation
Power on Integrated transmission machine
Choosing of compression manner
Choosing SSM
Setting of recording manner
Setting of antenna pointing mode
Power on RF and antenna
Setting of replaying manner
Power off Integrated transmission machine
Power off RF and antenna

## Slide 33: 4 Sequence of operation
Choosing SSM:
Main SSM
Standby SSM
Choosing compression manner:
Lossless compression
2:1 compression

## Slide 34: 4 Sequence of operation
Setting of recording manner:
Recording by sequence
Recording by address
Setting of replaying manner:
Replaying by sequence
Replaying by address

## Slide 35: 4 Sequence of operation
Setting of antenna pointing manner:
Independent calculation mode
Injection Pointing mode
Idle mode

## Slide 36: 4 Sequence of operation
No. | Item | Real Time | Record | Replay
1 | Power on Integrated transmission machine | • | • | •
2 | Choosing SSM |  | • | •
3 | Choosing of compression manner |  | • | 
4 | Setting of recording manner |  | • | 
5 | Power on RF and antenna | • |  | •
6 | Setting of antenna pointing mode | • |  | •
7 | Setting of replaying manner |  |  | •
8 | Power off RF and antenna | • |  | •
9 | Power off Integrated transmission machine | • | • | •

## Slide 37: CONTENTS
1
Composition and status of DTS in orbit
2
Working mode of DTS in orbit
3
Telecommand and telemetry of DTS
4
Sequence of operation
5
Important Notice
6
The Anomaly Operation in orbit

## Slide 38: 5 Important notice
The FPGA load time of integrated transmission machine is less than 15 seconds, namely 15 seconds after the Integrated transmission machine is powered on, following is allowed.
The FPGA load time of phase-array antenna is less than 8 seconds, namely 8 seconds after the phase-array antenna is powered on, the antenna starts to work normally.
The erasing time of main/standby SSM is less than 4.5 minutes, and the self-test time of main/standby SSM is less than 6 minutes.
The SSM main/standby state is exclusive in the process of one working task.

## Slide 39: 5 Important notice
The compression state is exclusive in the process of one working task, namely lossless compression or 2:1 compression.
SSM pointer restoring command must be executed before recording or replaying operation, similarly SSM pointer saving command must be executed after recording or replaying operation.
When the SSM is recording by sequence, recording pointer is increasing from 0 to (16383-number of bad blocks). The SSM stop recording when the SSM is full.

## Slide 40: 5 Important notice
When the SSM is replaying by sequence, replaying pointer is increasing from 0 to (16383-number of bad blocks). The SSM stop replaying when the SSM is already replayed over.
When the SSM is replaying by address, The SSM stop replaying when the replaying pointer arrives the designated ending address by block2.
Before the phase-array antenna uses injection pointing mode, the angle pointing data block(block4) must be injected in idle mode, namely turning off the Independent calculation mode.

## Slide 41: CONTENTS
1
Composition and status of DTS in orbit
2
Working mode of DTS in orbit
3
Telecommand and telemetry of DTS
4
Order of operation
5
Important Notice
6
The Anomaly Operation in orbit

## Slide 42: The Anomaly Operation in orbit
No | Failure Mode | Reason | Failure Analysis | Failure Detection | Action
1 | Integrated transmission machine doesn’t be powered on | Command can’t be transmitted or executed | TDS can’t work normally | FPGA Load state≠1: (Load failed) | inform DFH
2 | Several frames of the image date received by GS are missing or incorrect | Bad blocks occur in SSM | Partial image date received is missing or incorrect. | Check the image date received at ground station. | inform DFH

## Slide 43: The Anomaly Operation in orbit
No | Failure Mode | Reason | Failure Analysis | Failure Detection | Action
3 | RF signal level is lost or dropping | Transmitter or antenna can’t work normally | DTS can’t transmit image data or BER is increasing | The RF signal is lost or the signal received is lower. | inform DFH
4 | DTS doesn’t response to OBDH | The CAN bus in DTS works abnormally | One circle of satellite mission is failure. | DTS TM is not updating | inform DFH

## Slide 44: The Anomaly Operation in orbit
No | Failure Mode | Reason | Failure Analysis | Failure Detection | Action
5 | Antenna pointing abnormally | The software of antenna pointing failed | The GS can’t receive DTS RF signal form satellite | The TM ‘center angle of antenna’ and ‘Azimuth angle of antenna’ differ from emulation data | Inform DFH

## Slide 45
THANK YOU!