## Slide 1: OBDH In-Orbit Operation Instructions
DFH SATELLITE CO., LTD.
Oct, 2019

## Slide 2: Outline
  OBDH Specification
  Telecommand Format and Execution
  Time Calibration
  Time-tagged Command
  Time-tagged data block
  Relative time-tagged telecommand
  Thermal Control block
  Safety mode
  OBDH Critical TM
  In orbit operation

## Slide 3: Acronym list
Related to subsystem
OBDH：On Board Data Handling
OBC：On Board Computer
TCU：Thermal Control Unit
PCU: Power Control Unit
BMU: Battery Manage Unit
DTS: Data Transmission Subsystem
DCU: DTS Control Unit
FDIR: Failure Detection Isolation And Recovery
SEU: Single Event Upset

## Slide 4: Acronym list
Related to subsystem
AOCS: Attitude and Orbit Control Subsystem
AOCC: Attitude and Orbit Control Computer
MC: Multi-Spectrum Camera
PPS: Pulse per Second
GS: Ground Station
TTC: Time-Tagged Command
TTD: Time-Tagged Data Block
RTTC: Relative Time Tagged Telecommand

## Slide 5: PART 1: OBDH Specification
OBDH (onboard data handling subsystem) is kernel of satellite’s electronic system and responsible for satellite onboard working and information management. OBDH main Functions are as follows:
To receive Telecommands and data blocks from ground stations and distribute them to the satellite subsystems.
To collect the satellite telemetry data and send them to ground stations.
To manage the on-board time.

## Slide 6: PART 1: OBDH Specification
4. To provide the capability of receive and distribute the on-board commands and time-tagged commands.
5. To provide the capability of thermal control.
6. To store and restore the important data of AOCS.
7. To communicate with other subsystem via CAN bus.
8. To monitor the important parameters of satellite and manage the safe mode (FDIR) of satellite.

## Slide 7: PART 1: OBDH Specification
Type | Item | Parameter
Telemetry | Data Rate | 4096bps

## Slide 8: PART 1: OBDH Specification
Type | Item | Parameter
Telecommand | Number of Direct OC Command (from Responder) | 8
 | Number of OC Indirect Command (from OBC , Responder and PCU) | 40
 | Data Rate | 2000bps
 | Storage Capacity of time tagged Telecommand | 1000

## Slide 9: PART 1: OBDH Specification
Type | Item | Parameter
Timing System | On-board Timing reference | UTC
 | Time Precision | ≤5ms
Thermal control | Channels of heaters | 24
 | Channels of temperature measure | 24
Analog Channel | Number of analog measuring channel | 8

## Slide 10: PART 1: OBDH Specification
Type | Item | Parameter
CAN Bus | Bus type | CAN
 | Baud rate | 500kpbs
 | Bus utilization | ≤30%

## Slide 11: PART 2: Telemetry Management
Ground Users
Telemetry
Satellite
Data rate: 4096 bps

## Slide 12: PART 2: Telemetry Management
Telemetry(TM) is the only way for the GS to monitor the state of satellite. In ETRSS-1, telemetry function is fulfilled by OBC, CAN bus network, and the sub-computers in each subsystem.

## Slide 13: PART 2: Telemetry Management
Telemetry Information Flow
The subcomputer collects the telemetry of each subsystem, then the TM shall be collected through CAN bus and assembled into frames under protocol by OBC, and then is sent to Transponder. After being modulated into DPSK signal, the TM data is transmitted to the GS.

## Slide 14: PART 2: Telemetry Management
Telemetry Information Flow

## Slide 15: PART 2: Telemetry Management
    TM transfer frame format
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | … | … | 13 | 14 | 15 | 16 | 17 | … | 127
EB | 90 | AA | AA | AA | AA | ## | ## | ## | … | … | ## | ## | ## | ## | ## | … | ##
Attached Syn Marker |  | Reserved |  |  |  | Transfer Frame Primary Header |  | Fixed Format Telemetry |  |  |  | Master Channel Frame count | Virtual Channel Frame count | First Packet Header Pointer | Transfer Frame Data Field |  | 
2 |  | 4 |  |  |  | 2 |  | 6 |  |  |  | 1 | 1 | 1 | 111 |  | 

## Slide 16: PART 2: Telemetry Management
    Continuous Frame Format
TM Data transfer rate is 4096bps(512Byte/s), each second there will be 4 TM frames.
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | … | … | … | 13 | 14 | 15 | 16 | 17 | … | 127
EB | 90 | ## | ## | ## | ## | ## | ## | ## | ## | ## | ## | ## | M | FE | ## | ## | ## | ##
EB | 90 | ## | ## | ## | ## | ## | ## | ## | ## | ## | ## | ## | M+1 | FF | ## | ## | ## | ##
EB | 90 | ## | ## | ## | ## | ## | ## | ## | ## | ## | ## | ## | M+2 | 00 | ## | ## | ## | ##
EB | 90 | ## | ## | ## | ## | ## | ## | ## | ## | ## | ## | ## | M+3 | 01 | ## | ## | ## | ##
EB | 90 | ## | ## | ## | ## | ## | ## | ## | ## | ## | ## | ## | M+4 | 02 | ## | ## | ## | ##

## Slide 17: PART 2: Telemetry Management
Fixed Format Telemetry:
Fixed format telemetry is positioned in Secondary Header of the frame, which indicates the state of TM&TC channel, including satellite time, Transponder status.
Packet Telemetry:
Packet telemetry is positioned in transfer frame data field of the frame, including the other state of the satellite.

## Slide 18: PART 2: Telemetry Management
    TM packet format
Packet Primary Header (48 bits) |  |  |  |  |  |  | Packet Data Field
Packet Version Number | Packet Identification |  |  | Packet Sequence Control |  | Packet Data Length | User Data
 | Packet Type | Sec. Hdr. Flag | Application Process Identifier | Sequence Flags | Packet Sequence Count |  | 
3 bits | 1 bit | 1 bit | 11 bits | 2 bits | 14 bits | 16 bits | Variable Length
"000" | 0 | 0 |  | "11" |  |  | 

## Slide 19: PART 2: Telemetry Management
Packet Primary Header (48 bits) |  |  |  |  |  |  | Packet Data Field
Packet Version Number | Packet Identification |  |  | Packet Sequence Control |  | Packet Data Length | User Data
 | Packet Type | Sec. Hdr. Flag | Application Process Identifier | Sequence Flags | Packet Sequence Count |  | 
3 bits | 1 bit | 1 bit | 11 bits | 2 bits | 14 bits | 16 bits | Variable Length
"000" | 0 | 0 |  | "11" |  |  | 
Packet Version Number shall be set to “000”.
Packet Type shall be set to “0” for packet telemetry，used to distinguish with TC.
Secondary Header Flag shall be “0”, namely a packet secondary header is not present.

## Slide 20: PART 2: Telemetry Management
Application Process Identifier：used to identify TM packet, the highest bit: ‘0 ‘means real-time TM packet, while ‘1’ means delay time TM packet.
Sequence Flags set to “11”, means the packet contains unsegmented user data.
Packet Sequence Count：a counter for a packet.
Packet Data Length: equal to the size of packet data field minus 1.
Packet Primary Header (48 bits) |  |  |  |  |  |  | Packet Data Field
Packet Version Number | Packet Identification |  |  | Packet Sequence Control |  | Packet Data Length | User Data
 | Packet Type | Sec. Hdr. Flag | Application Process Identifier | Sequence Flags | Packet Sequence Count |  | 
3 bits | 1 bit | 1 bit | 11 bits | 2 bits | 14 bits | 16 bits | Variable Length
"000" | 0 | 0 |  | "11" |  |  | 

## Slide 21: PART 2: Telemetry Management
NO | TM Name | Packet I D | Packet length (bytes) | Data length (bytes) | Period | Delay Packet ID
1 | OBC fast | 20H | 49 | 50 | 1 | 420H
 | OBC fixed format TM | 30H | 23 | 24 | 1 | 430H
 | OBC Slow | 40H | 63 | 64 | 16 | 440H
 | OBC RTTC counter | 70H | 95 | 96 | 32 | 470H
 | OBC TTC | 90H | 61 | 62 | 32 | 490H
 | OBC bus counter | A0H | 57 | 58 | 16 | 4A0H
 | OBC uplink data block | B0H | VARIABLE | VARIABLE | 32 | /
 | OBC SRAM downlink | C0H | 57 | 68 | 1 | /
 | OBC data block | E0H | 65 | 66 | 32 | 4E0H
 | OBC RTTC | F0H | 255 | 256 | 32 | /

## Slide 22: PART 2: Telemetry Management
NO | TM Name | Packet ID | Packet length (bytes) | Data length (bytes) | Period | Delay Packet ID
2 | Transponder A fast TM | 22H | 15 | 16 | 1 | 422H
3 | Transponder B fast TM | 25H | 15 | 16 | 1 | 425H
4 | PCU fast TM | 23H | 11 | 12 | 32 | 423H
5 | PCU slow TM | 43H | 25 | 26 | 32 | 443H
6 | AOCs fast TM | 24H | 127 | 128 | 1 | 424H
7 | AOCs slow TM | 44H | 127 | 128 | 32 | 444H
8 | BMU fast TM | 28H | 13 | 14 | 4 | 428H
9 | TCU Anolog fast TM | 27H | 11 | 12 | 2 | 427H
10 | TCU Temperature slow TM | 47H | 63 | 64 | 32 | 447H
11 | TCU Configuration slow TM | 67H | 107 | 108 | 32 | 451H

## Slide 23: PART 2: Telemetry Management
NO | TM Name | Packet ID | Packet length (bytes) | Data length (bytes) | Period | Delay Packet ID
12 | OBC Back Data TM | 52 | 41 | 42 | 32 | 452H
13 | DTS fast TM | 2B | 7 | 8 | 2 | 42BH
14 | DTS slow TM | 4B | 15 | 16 | 16 | 44BH
15 | GPS fast TM | 2A | 19 | 20 | 2 | 42AH
16 | GPS status slow TM | 4A | 127 | 128 | 32 | 44AH
17 | GPS Orbit slow TM | 6A | 86 | 87 | 32 | 46AH
18 | MC fast TM | 2C | 28 | 29 | 2 | 42CH

## Slide 24: PART 2: Telemetry Management
OBC packet:
OBC generates the TM data of itself, then forms the OBC TM packet.
Subcomputer packet:
Subcomputer generates the TM data of itself, OBC collects the TM data from subcomputer via CAN bus, then forms the subcomputer TM packet.

## Slide 25: PART 2: Telemetry Management

## Slide 26: PART 2: Telemetry Management
For the orbit of ETRSS-1, the GS can not always track and get the TM data of the satellite, thus delayed Telemetry is used to monitor the state of the satellite when it is not traced by GS.
The delayed telemetry is sampled from real-time telemetry by OBC， and stored in the memory of OBC, which will be transferred to GS when ETRSS-1 can be tracked. The sample ratio can be set through indirect TC from GS.

## Slide 27: PART 2: Telemetry Management
Delayed Telemetry
Real time TM packet
Delayed TM packet saved in RAM.
Sampled ratio: from 1 to 255
sampled

## Slide 28: PART 2: Telemetry Management
If the interval of 2 tracks is 12 hours, the sample ration of ETRSS-1 is about 175, which is so large that sometimes the delayed TM can not reflects the state of the satellite accurately.

## Slide 29: PART 3: Telecommand Format and Execution
Ground Users
Telecommand
Satellite
Data rate: 2000 bps

## Slide 30: PART 3: Telecommand Format and Execution
Telecommand(TC) is the only way to control the satellite from GS. In ETRSS-1 OBDH subsystem, the function of TC is fulfilled by Transponder and OBC.

## Slide 31: PART 3: Telecommand Format and Execution
    From the aspect of the way of execution, TC can be classified as direct TC, indirect TC and indirect TC & data block.
TYPES | DESCRIPTIONS
Direct TC | Received, decoded, authenticated by Transponder, and Transponder will execute the TC in the way of OC.
Indirect TC & Data block | Received, decoded by Transponder, then the TC is sent to OBC, OBC executes the TC or sends the TC to the corresponding device via CAN bus, and the device will execute the TC.

## Slide 32: PART 3: Telecommand Format and Execution
Telecommand Information Flow
TC data shall be uploaded from GS, received by USB transponder. After demodulation and analysis, direct TC will be executed immediately, all the indirect TC and data block will be transmitted to OBC. OBC shall handle them and then transmit them to different units through CAN bus.

## Slide 33: PART 3: Telecommand Format and Execution
    TC format
    Direct TC
Satellite address synchronization word: 7718H
PSK Preamble | TC code
PSK Preamble | TC Code |  | 
 | Satellite address synchronization word | Mode word | Execution Code
128bits | 16bits | 8bits | 72bits

## Slide 34: PART 3: Telecommand Format and Execution
Ground
Direct TC
OC

## Slide 35: PART 3: Telecommand Format and Execution
    Indirect TC & Data block
PSK Preamble | TC Code |  |  | 
 | Satellite address synchronization word | Mode word | Execution Code (TC Transfer Frame) | CRC
128bits | 16bits | 8bits | 128/512/1024/2048 bits | 16bits

## Slide 36: PART 3: Telecommand Format and Execution
Mode word:
5AH | The length of executing code is 128bits(16bytes)
69H | The length of executing code is 512bits(64bytes)
99H | The length of executing code is 1024bits(128bytes)
A5H | The length of executing code is 2048bits(256bytes)

## Slide 37: PART 3: Telecommand Format and Execution
    TC transfer frame format
Transfer Frame Primary Header (40 bits) |  |  |  |  |  |  |  | Transfer Frame Data Field | Frame Error Control Field
Transfer Frame Version Number | RSVD. SPARE | RSVD. SPARE | RSVD. SPARE | Spacecraft ID | Virtual Channel ID | Frame Length | Frame Sequence Number |  | 
2 bits | 1 bit | 1 bit | 2 bits | 10 bits | 6 bits | 10 bits | 8 bits |  | 16 bits
00 | 1 | 0 | 00 | 00 0000 00 00 |  | 0x0F, 0X3F, 0X7F, 0XFF | 00 | 9,57,121,249 | XOR
Frame Error Control Field is used to check Transfer Frame by Calculate the word XOR value of Transfer Frame Primary Header and Transfer Frame Data Field.

## Slide 38: PART 3: Telecommand Format and Execution
    Virtual Channel ID
Subcomputer | Channel identification
OBC | 00H (00 0000b)
Transponder A | 02H (00 0010b)
PCU | 03H (00 0011b)
AOCC | 04H (00 0100b)
Transponder B | 05H (00 0101b)
PCU | 07H (00 0111b)
GPS | 0AH (00 1010b)
DCU | 0BH (00 1011b)
MC | 11H (01 0001b)
BMU | 12H (01 0010b)
NOTE: Virtual Channel ID is used for data block, all indirect TC from GS, Virtual Channel ID is always 0.

## Slide 39: PART 3: Telecommand Format and Execution
Transfer Frame Primary Header (40 bits) |  |  |  |  |  |  |  | Transfer Frame Data Field | Frame Error Control Field
Transfer Frame Version Number | Bypass Flag | Control COMMAND Flag | RSVD. SPARE | Spacecraft ID | Virtual Channel ID | Frame Length | Frame Sequence Number |  | 
2 bits | 1 bit | 1 bit | 2 bits | 10 bits | 6 bits | 10 bits | 8 bits |  | 16 bits
00 | 1 | 0 | 00 | XX | XX | 0x0F, 0X3F, 0X7F, 0XFF | 0 | 9,57,121,249 | XOR Exclusive Or
Type ID of Command | Data
1Bytes | 8，56，120，248 Bytes
In OBC, Transfer Frame Data Field divided into two parts.
Type ID of Command indicates which type this command belongs to

## Slide 40: PART 3: Telecommand Format and Execution
    OBC Data Type
20H | Indirect TC block
40H | Data block
80H | TTC
A0H | RTTC
C0H | TTD
D0H | PMC gain
E0H | Patch code
    For OBC and subcomputer

## Slide 41: PART 3: Telecommand Format and Execution
NO | DATA | DESCRIPTION
0 | 20H | IDENTIFICATION
1 | m | m=6
2 | 00H | reserved
3 | n | n=1
4 | ##H | Command
5 | ##H | 
6 | ##H | 
7 | ##H | 
8 | AAH | reserved
Format of Indirect TC block
Example: 20 06 00 01 00 02 00 00 AA

## Slide 42: PART 3: Telecommand Format and Execution
Transfer Frame Primary Header (40 bits) |  |  |  |  |  |  |  | Transfer Frame Data Field | Frame Error Control Field
Transfer Frame Version Number | Bypass Flag | Control COMMAND Flag | RSVD. SPARE | Spacecraft ID | Virtual Channel ID | Frame Length | Frame Sequence Number |  | 
2 bits | 1 bit | 1 bit | 2 bits | 10 bits | 6 bits | 10 bits | 8 bits |  | 16 bits
00 | 0 | 0 | 00 | 00 0001 0001 | XX | 0x0F, 0X3F, 0X7F, 0XFF | 0 | 9,57,121,249 | XOR Exclusive Or
    Example of Indirect TC block in transfer frame format
00 11 00 0F 00 20 06 00 01 00 02 00 00 AA 05 94
Indirect TC block Virtual Channel ID is always 0

## Slide 43: PART 3: Telecommand Format and Execution
Example of Indirect TC block with CRC
77 18 5A 00 11 00 0F 00 20 06 00 01 00 02 00 00 AA 05 94 18 ED
TC Code |  |  | 
Satellite address synchronization word | Mode word | Execution Code (TC Transfer Frame) | CRC
16bits | 8bits | 128/512/1024/2048 bits | 16bits

## Slide 44: PART 3: Telecommand Format and Execution
Transfer Frame Primary Header (40 bits) |  |  |  |  |  |  |  | Transfer Frame Data Field | Frame Error Control Field
Transfer Frame Version Number | Bypass Flag | Control COMMAND Flag | RSVD. SPARE | Spacecraft ID | Virtual Channel ID | Frame Length | Frame Sequence Number |  | 
2 bits | 1 bit | 1 bit | 2 bits | 10 bits | 6 bits | 10 bits | 8 bits |  | 16 bits
00 | 0 | 0 | 00 | 00 0001 0001 | XX | 0x0F, 0X3F, 0X7F, 0XFF | 0 | 9,57,121,249 | XOR Exclusive Or
    Example of subcomputer data block in transfer frame format
00 11 10 0F 00 00 00 00 00 00 00 00 00 00 10 1E
AOCC data block
Virtual channel ID is 4

## Slide 45: PART 3: Telecommand Format and Execution
Example of Indirect TC block with CRC
77 18 5A 00 11 10 0F 00 00 00 00 00 00 00 00 00 00 10 1E 7D 55
TC Code |  |  | 
Satellite address synchronization word | Mode word | Execution Code (TC Transfer Frame) | CRC
16bits | 8bits | 128/512/1024/2048 bits | 16bits

## Slide 46: PART 3: Telecommand Format and Execution
Ground
Indirect TC(data)
CAN BUS

## Slide 47: PART 3: Telecommand Format and Execution
Ground
Indirect TC(OC)
OC

## Slide 48: PART 3: Telecommand Format and Execution
Criterion of receive Indirect TC block from GS
XS001 ++,
If the Indirect TC belongs to subcomputer, XS002++, XB001++，Send to subcomputer counter in Packet A0H ++，
if subcomputer receive correctly, XS003++, XB002++, Subcomputer respond counter in Packet A0H ++
NOTE: XS001 is the most important criterion of satellite receive indirect TC/data block from GS.

## Slide 49: PART 3: Telecommand Format and Execution
Example: Indirect TC/ data block sends to AOCC from GS
Receive an indirect TC from GS
XS001++
Is OBC TC?
OBC execute the TC
Y
N
XS002++
XB001++
OBC sent an indirect TC to sub-computer
XS003++
XB002++
Sub-computer received an indirect TC

## Slide 50: PART 4: Time Calibration
OBDH time is provided by OBC. The time zero reference shall be 1st January 2009, 00 hour: 00minute: 00 second: 00millisecond (UTC). That means at that time the on-board time code is all zero.

## Slide 51: PART 4: Time Calibration
There are several ways to correct the on board time, Using GPS time self-calibration mode, Using GPS setting time (one time mode) and GS telecommand time calibration mode.
GS telecommand time calibration includes one time adjustment (add or subtract) to the current on board time, uniform time correction and ground time setting.
In orbit, we suggest to use GPS time self-calibration as long as GPS is correct.

## Slide 52: PART 4: Time Calibration
GPS time self-calibration mode-default mode in orbit
.
Compare OBC time and GPS time, then calibrate OBC time.
GPS
OBC
Collect/polling GPS UTC time periodically
GPS time

## Slide 53: PART 4: Time Calibration
GPS setting time.
OBC using GPS time directly.
GPS
OBC
Collect/polling GPS UTC time only one time
GPS time

## Slide 54: PART 4: Time Calibration
One time adjustment (add or subtract) to the current on board time.
The time difference between the ground and satellite should be calculated by ground station and be transmitted through the uplink channel. OBC performs immediately the operation of addition between the on board time and the time difference in order to aim at the ground.

## Slide 55: PART 4: Time Calibration
One time adjustment data block format.
NO | DATA | DESCRIPTION
0 | 40H | IDENTIFICATION
1 | 11H | ASSISTANT SYMBOL
2 | 01H | TYPE
3 | ##H | ADJUST SECOND Complementary code, HIGH BYTE FIRST
4 | ##H | 
5 | ##H | 
6 | ##H | 
7 | ##H | ADJUST MILLSECOND TRUE FORM, HIGH BYTE FIRST
8 | ##H | 

## Slide 56: PART 4: Time Calibration
One time adjustment data block example
NO | DATA | DESCRIPTION |  | 
0 | 40H | IDENTIFICATION | 40 | 
1 | 11H | ASSISTANT SYMBOL | 11 | 
2 | 01H | TYPE | 01 | 
3 | ##H | ADJUST SECOND Complementary code, HIGH BYTE FIRST | 00 00 00 0A | +10s
4 | ##H |  |  | 
5 | ##H |  |  | 
6 | ##H |  |  | 
7 | ##H | ADJUST MILLSECOND TRUE FORM, HIGH BYTE FIRST | 00 64 | 100ms
8 | ##H |  |  | 
One time adjustment 10.1s:
77 18 5A 00 11 00 0F 00 40 11 01 00 00 00 0A 00 64 11 31 3E

## Slide 57: PART 4: Time Calibration
One time adjustment -10.1s:
77 18 5A 00 11 00 0F 00 40 11 01 FF FF FF F5 03 84 12 D1 A4 80
NO | DATA | DESCRIPTION |  | 
0 | 40H | IDENTIFICATION | 40 | 
1 | 11H | ASSISTANT SYMBOL | 11 | 
2 | 01H | TYPE | 01 | 
3 | ##H | ADJUST SECOND Complementary code, HIGH BYTE FIRST | FF FF FF F5 | -11s
4 | ##H |  |  | 
5 | ##H |  |  | 
6 | ##H |  |  | 
7 | ##H | ADJUST MILLSECOND TRUE FORM, HIGH BYTE FIRST | 03 84 | 900ms
8 | ##H |  |  | 

## Slide 58: PART 4: Time Calibration
Uniform time correction .
The uniform time correction is to add or subtract periodically one millisecond of on board time to eliminate the predicted time error. The interval to perform the uniform time correction is the range from 1 to 0xFFFFFF seconds.

## Slide 59: PART 4: Time Calibration
Uniform time correction Format.
NO | DATA | DESCRIPTION
0 | 40H | IDENTIFICATION
1 | 11H | ASSISTANT SYMBOL
2 | 02H | TYPE
3 | ##H | PERIOD TIME(Sec, >=1) TRUE FORM, HIGH BYTE FIRST
4 | ##H | 
5 | ##H | 
6 | ##H | PERIOD TIME(ms, <1000) TRUE FORM, HIGH BYTE FIRST
7 | ##H | 
8 | ##H | 00H: STOP; 66H: +1ms 99H: -1ms

## Slide 60: PART 4: Time Calibration
Uniform time correction example: 256.01s add 1ms
NO | DATA | DESCRIPTION |  | 
0 | 40H | IDENTIFICATION | 40 | 
1 | 11H | ASSISTANT SYMBOL | 11 | 
2 | 02H | TYPE | 02 | 
3 | ##H | PERIOD TIME(Sec, >=1) TRUE FORM, HIGH BYTE FIRST | 00 01 00 | 256s
4 | ##H |  |  | 
5 | ##H |  |  | 
6 | ##H | PERIOD TIME(ms, <1000) TRUE FORM, HIGH BYTE FIRST | 00 0A | 10ms
7 | ##H |  |  | 
8 | ##H | 00H: STOP; 66H: +1ms 99H: -1ms | 66 | +1ms
77 18 5A 00 11 00 0F 00 40 11 02 00 01 00 00 0A 66 1B 3B 93 FF

## Slide 61: PART 4: Time Calibration
Uniform time correction example: 1000.3s subtract 1ms
NO | DATA | DESCRIPTION |  | 
0 | 40H | IDENTIFICATION | 40 | 
1 | 11H | ASSISTANT SYMBOL | 11 | 
2 | 02H | TYPE | 02 | 
3 | ##H | PERIOD TIME(Sec, >=1) TRUE FORM, HIGH BYTE FIRST | 00 03 E8 | 1000s
4 | ##H |  |  | 
5 | ##H |  |  | 
6 | ##H | PERIOD TIME(ms, <1000) TRUE FORM, HIGH BYTE FIRST | 01 2C | 300ms
7 | ##H |  |  | 
8 | ##H | 00H: STOP; 66H: +1ms 99H: -1ms | 99 | -1ms
77 18 5A 00 11 00 0F 00 40 11 02 00 03 E8 01 2C 99 D5 C7 1B 4B

## Slide 62: PART 4: Time Calibration
Uniform time correction stop
NO | DATA | DESCRIPTION | 
0 | 40H | IDENTIFICATION | 40
1 | 11H | ASSISTANT SYMBOL | 11
2 | 02H | TYPE | 02
3 | ##H | PERIOD TIME(Sec, >=1) TRUE FORM, HIGH BYTE FIRST | 00 00 00
4 | ##H |  | 
5 | ##H |  | 
6 | ##H | PERIOD TIME(ms, <1000) TRUE FORM, HIGH BYTE FIRST | 00 00
7 | ##H |  | 
8 | ##H | 00H: STOP; 66H: +1ms 99H: -1ms | 00
77 18 5A 00 11 00 0F 00 40 11 02 00 00 00 00 00 00 11 5C 99 74

## Slide 63: PART 4: Time Calibration
Ground time setting
Ground time setting means setting the on board time directly according to forward data block .
NO | DATA | DESCRIPTION
0 | 40H | IDENTIFICATION
1 | 11H | ASSISTANT SYMBOL
2 | 03H | TYPE
3 | ##H | ADJUST SECOND TRUE FORM, HIGH BYTE FIRST
4 | ##H | 
5 | ##H | 
6 | ##H | 
7 | ##H | ADJUST MILLSECOND TRUE FORM, HIGH BYTE FIRST
8 | ##H | 
Note：The time point ground set the OBC time and collect the TM is not same, the TM of OBC time will be several hundred millisecond later than the time ground set.

## Slide 64: PART 4: Time Calibration
Ground time setting example：65536s 256ms
NO | DATA | DESCRIPTION |  | 
0 | 40H | IDENTIFICATION | 40 | 
1 | 11H | ASSISTANT SYMBOL | 11 | 
2 | 03H | TYPE | 03 | 
3 | ##H | ADJUST SECOND TRUE FORM, HIGH BYTE FIRST | 00 01 00 00 | 65536s
4 | ##H |  |  | 
5 | ##H |  |  | 
6 | ##H |  |  | 
7 | ##H | ADJUST MILLSECOND TRUE FORM, HIGH BYTE FIRST | 01 00 | 256ms
8 | ##H |  |  | 
77 18 5A 00 11 00 0F 00 40 11 03 00 01 00 00 01 00 10 5C 8F B3

## Slide 65: PART 4: Time Calibration
Time-tagged Command.
Each TTC is composed with 8 bytes. The first 4 bytes is UTC time to be executed, and the last 4 bytes is execution code (Indirect TC CODE).
  Ground Station
Batch of TTCs
  OBC
Compare TTC time to Onboard time
  Subcomputer
Saved in OBC SRAM

## Slide 66: PART 4: Time Calibration
TTC data block format.
NO | DATA | DESCRIPTION
0 | 80H | IDENTIFICATION
1 | m | LENGTH
2 | 00H | RESERVE WORD
3 | n | COMMAND COUNT
4 | ##H | Task ID1
5 | ##H | 
6 | ##H | UTC TIME1
7 | ##H | 
8 | ##H | 
 | ##H | 
 | ##H | EXECUTION CODE1
 | ##H | 
 | ##H | 
 | ##H | 
 | ##H | Task ID2
 | ##H | 
 | ##H | UTC TIME2
 | ##H | 
 | ##H | 
 | ##H | 
 | ##H | EXECUTION CODE2
 | ##H | 
 | ##H | 
 | ##H | 
 |  | …
 |  | …
 | ##H | 
 | ##H | Task IDn
 | ##H | 
 | ##H | UTC TIMEn
 | ##H | 
 | ##H | 
 | ##H | 
 | ##H | EXECUTION CODEn
 | ##H | 
m+1 | ##H | 
m+2 | ##H | 
 | AAH | RESERVED
 | … | 
 | AAH | 
L-1 | AAH | 

## Slide 67: PART 4: Time Calibration
TTC data block format.
77 18 69
00 11 00 3F 00
80
16 = （2*10+2）
00
02
01
10 06 DB FA
13 12 02 AA
01
10 06 DC 04
00 01 80 00
AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA 77 83 33 C9
NO | DATA | DESCRIPTION
0 | 80H | IDENTIFICATION
1 | m | LENGTH
2 | 00H | RESERVE WORD
3 | n | COMMAND COUNT
4 | ##H | Task ID1
5 | ##H | 
6 | ##H | UTC TIME1
7 | ##H | 
8 | ##H | 
 | ##H | 
 | ##H | EXECUTION CODE1
 | ##H | 
 | ##H | 
 | ##H | 
 | ##H | Task ID2
 | ##H | 
 | ##H | UTC TIME2
 | ##H | 
 | ##H | 
 | ##H | 
 | ##H | EXECUTION CODE2
 | ##H | 
 | ##H | 
 | ##H | 
 |  | …

## Slide 68: PART 4: Time Calibration
TTC data block insert rule.
No | New TTC Data block |  | TTC in buffer | Executing status
1 | Max time | < | Min time | New TTC block insert in front of Min time command
2 | Min time | > | Max time | New TTC block insert in behind of Max time command
3 | Min time | > | Command n time | New TTC block insert between command n and command n+1
 | Max time | < | Command n+1 time | 
4 | Other condition |  |  | TTC error

## Slide 69: PART 5: Time-tagged data block
Time-tagged data block.
TTD is extension of TTC. Each TTD is composed with 64 bytes. The first 2 bytes is Task ID, the next is UTC time and virtual channel ID , and the last 57bytes is TC data. (For TTC is 4 bytes indirect TC)
  Ground Station
Batch of TTDs
  OBC
Compare TTD time to Onboard time
  Subcomputer
Saved in OBC SRAM

## Slide 70: PART 5: Time-tagged data block
TTD data block format.
NO | DATA | DESCRIPTION
0 | C0H | IDENTIFICATION
1 | m | Length m=64n+2
2 | 00H | reserved
3 | n | Command counter
4 | ##H | Task ID 1
5 | ##H | 
6 | ##H | Data block time 1 (s)
7 | ##H | 
8 | ##H | 
9 | ##H | 
10 | ##H | Data block channel identification 1
12 | ##H | Data block code 1
13 | ##H | 
14 | ##H | 
15 | ##H | 
16 | ##H | 
… | … | 
66 | ##H | 
67 | ##H | 
 |  | …
 | ##H | 
 | ##H | Task ID n
 | ##H | 
 | ##H | Data block time n (s)
 | ##H | 
 | ##H | 
 | ##H | 
 | ##H | Data block channel identification n
 | ##H | Data block code n
 | ##H | 
 | ##H | 
 | ##H | 
 | ##H | 
 | ##H | 
 | … | 
m | ##H | 
m+1 | ##H | 
 | AAH | reserved
 | … | 
 | AAH | 
L-1 | AAH | 

## Slide 71: PART 5: Time-tagged data block
TTD data block format.
77 18 A5
00 11 00 FF 00
C0
42
00
01
01
00 01 12 13
06
01 02 03 04 05 06 07 08 09
AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA AA 80 23 41 BB
NO | DATA | DESCRIPTION
0 | C0H | IDENTIFICATION
1 | m | Length m=64n+2
2 | 00H | reserved
3 | n | Command counter
4 | ##H | Task ID 1
5 | ##H | 
6 | ##H | Data block time 1 (s)
7 | ##H | 
8 | ##H | 
9 | ##H | 
10 | ##H | Data block channel identification 1
12 | ##H | Data block code 1
13 | ##H | 
14 | ##H | 
15 | ##H | 
16 | ##H | 
… | … | 
66 | ##H | 
67 | ##H | 

## Slide 72: PART 5: Time-tagged data block
TTD data block insert rule.
No | New TTD Data block |  | TTD in buffer | Executing status
1 | Max time | < | Min time | New TTD block insert in front of Min time command
2 | Min time | > | Max time | New TTD block insert in behind of Max time command
3 | Min time | > | Command n time | New TTD block insert between command n and command n+1
 | Max time | < | Command n+1 time | 
4 | Other condition |  |  | TTD error

## Slide 73: PART 6: Relative time-tagged telecommand
Relative time-tagged telecommand.
Each RTTC is composed with 6 bytes. The first 2 bytes is the time relative to start time, and the last 4 bytes is TC code (Indirect TC CODE).
  Ground Station
A group RTTC
  OBC
Compare RTTC time with relative counter to start time
  Subcomputer
Saved in OBC EEPROM

## Slide 74: PART 6: Relative time-tagged telecommand
TTC and RTTC comparison
NO | TTC | RTTC
1 | Saved In SRAM | Saved in EEPROM
2 | Be clear after execution | Not clear after execution
3 | Support 1000 TTC saved in OBC at most. | Max 32 groups, and each group can store 38 TCs
4 | Compared to absolute UTC time | Compared to relative the time of start RTTC group
5 | Cooperated with RTTC used for mission operation | General used fixed command sequence ,like payload power on /power off sequence

## Slide 75: PART 6: Relative time-tagged telecommand
Each group of RTTCs can be divided into 2 segments with ID 1 and 2. Generlly segments 1 used for payload power on and segments 2 used for power off. And the time between segments 1 and segments 2 can be controlled by the TC of start RTTC.
Segment 1
Segment 1
Segment 1
△t
Segment 2
Segment 2
Segment 2

## Slide 76: PART 6: Relative time-tagged telecommand
RTTC data block format.
NO | DATA | LENGTH | DESCRIPTION
0 | A0H | 1 | IDENTIFICATION
1 | ##H | 1 | group number
2 | ##H | 1 | Command counter
3 | ##H | 8 | reserved
4 | ##H | 2 | High 4bit, segment id Low 12bit, TC ∆time
 | ##H | 4 | TC code 1
 | ##H | 2 | High 4bit, segment id Low 12bit, TC ∆time
 | ##H | 4 | TC code 2
… | … | … | …
 | ##H | 2 | High 4bit, segment id Low 12bit, TC ∆time
L-1 | ##H | 4 | TC code n

## Slide 77: PART 6: Relative time-tagged telecommand
NO | DATA | LENGTH | DESCRIPTION
0 | A0H | 1 | IDENTIFICATION
1 | ##H | 1 | group number
2 | ##H | 1 | Command counter
3 | ##H | 8 | reserved
4 | ##H | 2 | High 4bit, segment id Low 12bit, TC ∆time
 | ##H | 4 | TC code 1
 | ##H | 2 | High 4bit, segment id Low 12bit, TC ∆time
 | ##H | 4 | TC code 2
… | … | … | …
 | ##H | 2 | High 4bit, segment id Low 12bit, TC ∆time
L-1 | ##H | 4 | TC code n
RTTC data block format.
86 EA 69
20 00 00 3F 00
A0
02
04
00 00 00 00 00 00 00 00
10 00 03 05 AA AA
10 01 03 0A AA AA
20 02 12 28 AA AA
20 04 12 2E CC AA
AA AA AA AA AA
AA AA AA AA AA
AA AA AA AA AA
AA AA AA AA AA
AA AA EE 3F 83 4A

## Slide 78: PART 7: Thermal Control block
Open-Loop
Indirect TC uploaded from ground control heater to on or off.
Close-Loop
Close-loop mode contains two sub-modes, Proportional control mode and threshold control mode.

## Slide 79: PART 7: Thermal Control block
Close-Loop-Threshold control
When the temperature is below the low threshold, the heater will be switched on. When the temperature exceeds the high threshold, the heater will be switched off.
Close-Loop-Proportional control
When the temperature is below the low threshold, the heater will be switched on. When the temperature exceeds the high threshold, the heater will be switched off.
When the temperature is between the lower threshold and upped threshold, the time of the heater switched on in one second can be calculate by the formula as follows:
HEATING_TIME_RATIO = (HIGH_THR – Tmperature)/(HIGH_THR – LOW_THR)

## Slide 80: PART 7: Thermal Control block
NO |  | 
1 | 00H | 
2 | 00H | 
3 | ##H | Heater selection(1-24)
4 | ##H | B5B4：10: close-loop，01: open-loop B7~B6： In close-loop mode： 10：Proportional control 01：Threshold control In open-loop mode： 01：heater on 10：heater off B3~B0： In close-loop mode： 00H：min temperature control 0FH：average temperature control 01H：use thermistor 1 control temperature 02H：use thermistor 2 control temperature 03H：use thermistor 3 control temperature
5 | ##H | Temperature High Threshold (AAH in open-loop mode)
6 | ##H | 
7 | ##H | Temperature Low Threshold (AAH in open-loop mode)
8 | ##H | 
9 | AAH | 

## Slide 81: PART 7: Thermal Control block
NO |  |  |  | 
1 | 00H |  | 00 | 
2 | 00H |  | 00 | 
3 | ##H | Heater selection(1-24) | 01 | Loop 1
4 | ##H | B5B4：10: close-loop，01: open-loop B7~B6： In close-loop mode： 10：Proportional control 01：Threshold control In open-loop mode： 01：heater on 10：heater off B3~B0： In close-loop mode： 00H：min temperature control 0FH：average temperature control 01H：use thermistor 1 control temperature 02H：use thermistor 2 control temperature 03H：use thermistor 3 control temperature | 91 | 91H:1001 0001 close-loop mode Proportional control Use thermistor 1 control temperature
5 | ##H | Temperature High Threshold (AAH in open-loop mode) | 05 CA | Temperature High Threshold
6 | ##H |  |  | 
7 | AAH | Temperature Low Threshold (AAH in open-loop mode) | 05 F0 | Temperature Low Threshold
8 | AAH |  |  | 
9 | AAH |  | AA | 

## Slide 82: PART 8: Safe Mode
OBDH subsystem monitors the required parameters and manages the safe mode of the satellite. OBDH is mainly responsible for system level FDIR to make sure the safety of satellite system.
The TMs monitored by OBDH directly or indirectly include battery voltage, battery temperature, the mode of AOCS, and the communication status of some units.

## Slide 83: PART 8: Safe Mode
OBDH monitors the critical TMs (such as the status of power supply system and AOCS). When the critical TMs become abnormal, OBDH sends safe command sequence, such as turning off the payload, making sure the satellite energy is preserved safely.
When safe mode occurs, the corresponding safe mode execute counter will change, DFH should be Informed to deal with it.

## Slide 84: PART 8: Safe Mode
Safety mode implemented by OBC
NO | Safety Mode | Abnormal | Safety measure and safety TM | Entrty Criterion
1 | TTC Check Error Safety Mode | TTC check error | 1) Reinitialize TTC 2) Run RTTC group 13 to send payload power off command sequence. 3) Set the sign to “TTC Check Error Safety Mode” | XH164 (TTC Check Error Safety Mode COUNTER) change
2 | TTD Check Error Safety Mode | TTD check error | 1) Reinitialize TTD 2) Run RTTC group 13 to send payload power off command sequence. 3)Set the sign to “TTD Check Error Safety Mode” | XH165 (TTD Check Error Safety Mode COUNTER) change

## Slide 85: PART 8: Safe Mode
Safety mode implemented by OBC
NO | Safety Mode | Abnormal | Safety measure and safety TM | Entrty Criterion
3 | Energy protect Safety Mode( triggered by PCU) | P43W8B6B6=11b for 3 times | 1) Run RTTC group 10 to send payload power off command sequence. 2) Set the sign to “Energy protect Safety Mode( triggered by PCU)” | XH166(Energy protect Safety Mode triggered by PCU COUNTER ) change
4 | AOCS Global Attitude Acquisition Safety Mode COUNTER | P24W4B7~B4 = 02H for 10 times | 1) Run RTTC group 8 to send payload power off command sequence. 2)Set the sign to “AOCS Global Attitude Acquisition Safety Mode ” | XH167(AOCS Global Attitude Acquisition Safety Mode COUNTER) change

## Slide 86: PART 8: Safe Mode
Safety mode implemented by OBC
5 | AOCS Stop Control Safety Mode | P24W4B7~B4 = 0CH for 10 times | 1) Run RTTC group 9 to send payload power off command sequence. 2) Set the sign to “AOCS Stop Control Safety Mode” | XH168 change
6 | Energy warning Safety Mode 1 | P43W8B5B1 = 11b for 3 times | 1) Run RTTC group 10 to send payload power off command sequence. 2)Set the sign to “Energy warning Safety Mode 1” | XH169 change
7 | Energy warning Safety Mode 2 | P43W8B4B0 = 11b for 3 times | 1) Run RTTC group 10 to send payload power off command sequence. 2) Set the sign to “Energy warning Safety Mode 2” | XH170 change
8 | CCD temperature Safety Mode | P47W40~W42B11~B0<Limit Temperature for 3 times | 1) Run RTTC group 11 to send payload power off command sequence. 2)Set the sign to “CCD temperature Safety Mode” | XH171 change

## Slide 87: PART 8: Safe Mode
Safety mode implemented by OBC
9 | Phased array antenna temperature Safety Mode | P47W13~W15B23~B12<Limit Temperature for 3 times | 1) Run RTTC group 12 to send Phased array antenna power off command sequence. 2) Set the sign to “Phased array antenna temperature Safety Mode” | XH172 change
10 | Phased array antenna working timeout Safety Mode | P27W6~W8B11~B0>Limit Value for 600s | 1) Run RTTC group 12 to send Phased array antenna power off command sequence. 2)Set the sign to “Phased array antenna working timeout Safety Mode” | XH173 change
11 | TC monitor Timeout Safety Mode | KSM35-01 is not received for 72 hours | 1) Run RTTC group 14 to send reset Transponder A and Transponder B command sequence. 2) Set the sign to “TC monitor Timeout Safety Mode” | XH175 change

## Slide 88: PART 8: Safe Mode
Communication Safety mode implemented by OBC
1 | Transponder A Communication Safety Mode | 100 times abnormal communication | 1) Run RTTC group 1 to send Transponder A power off, and then power on. 2) Set the sign to “Transponder A Communication Safety Mode” | XH032 change
2 | PCU Communication Safety Mode | 100 times abnormal communication | 1) Run RTTC group 2 to send PCU Sub-computer B on/A off. 2) Set the sign to “PCU Communication Safety Mode” | XH033 change
3 | Responder B Communication Safety Mode | 100 times abnormal communication | 1) Run RTTC group 4 to send Transponder b power off, and then power on. 2) Set the sign to “Transponder b Communication Safety Mode” | XH035 change
4 | TCU Communication Safety Mode | 100 times abnormal communication | 1) Run RTTC group 5 to send TCU Sub-computer A off, and then B on 2) Set the sign to “TCU Sub-computer communication Safety Mode” | XH036 change

## Slide 89: PART 8: Safe Mode
Safety mode implemented by OBC
5 | BMU Communication Safety Mode | 100 times abnormal communication | 1) Run RTTC group 6 to send BMU Sub-computer power off, and then power on 2) Set the sign to “BMU Communication Safety Mode” | XH037 change
6 | GPS Communication Safety Mode | 100 times abnormal communication | 1) Run RTTC group 2 to send GPS receiver A off, B off, and then GPS B on. 2) Set the sign to “GPS Communication Safety Mode” | XH038 change

## Slide 90: PART 9: OBDH Critical TM
NO | TM Name | Packet I D | Packet length (bytes) | Data length (bytes) | Period | Delay Packet ID
1 | OBC fast | 20H | 49 | 50 | 1 | 420H
 | OBC fixed format TM | 30H | 23 | 24 | 1 | 430H
 | OBC Slow | 40H | 63 | 64 | 16 | 440H
 | OBC RTTC counter | 70H | 95 | 96 | 32 | 470H
 | OBC TTC | 90H | 61 | 62 | 32 | 490H
 | OBC bus counter | A0H | 57 | 58 | 16 | 4A0H
 | OBC uplink data block | B0H | VARIABLE | VARIABLE | 32 | /
 | OBC SRAM downlink | C0H | 57 | 68 | 1 | /
 | OBC data block | E0H | 65 | 66 | 32 | 4E0H
 | OBC RTTC | F0H | 255 | 256 | 32 | /
All the TM packets of OBC are showed as follows

## Slide 91: PART 9: OBDH Critical TM
Packet 20H and packet 40H contain most of the OBDH Critical information In-orbit.
NO | TM Name | Packet I D | Packet length (bytes) | Data length (bytes) | Period | Delay Packet ID
1 | OBC fast | 20H | 49 | 50 | 1 | 420H
 | OBC Slow | 40H | 63 | 64 | 16 | 440H

## Slide 92: PART 9: OBDH Critical TM
Parameter Number | Parameter Name | Work Range | Description
XS001 | TC_COUNTER | 0~0xFFFF | +1/ (Indirect TC, Data block)
XS027 | TTC_Task_Permission_Status | 1:Enabled | Should be Enabled in normal mode. Please check whether safety mode is triggered when this TM becomes Disabled
XS029 | TTC_Check_Status | 0:normal | Maybe become error status caused by SEU(small probability event)
XS033 | TTD_Check_Status | 0:normal | Maybe become error status caused by SEU(small probability event)
XS038 | TTC_Insert_Status | 0x66:Normal | Reference Part 10
XS042 | TTD_Insert_Status | 0x66:Normal | Reference Part 10
Packet 20H

## Slide 93: PART 9: OBDH Critical TM
Parameter Number | Parameter Name | Work Range | Description
XS110 | GPS_Communication_Safety_Mode_Status | 0:Normal | 
XS111 | Battery_Subcomputer_Communication_Safety_Mode_Status | 0:Normal | 
XS112 | TCU_Communication_Safety_Mode_Status | 0:Normal | 
XS113 | Transponder_B_Communication_Safety_Mode_Status | 0:Normal | 
XS115 | PCU_Communication_Safety_Mode_Status | 0:Normal | 
XS116 | Transponder_A_Communication_Safety_Mode_Status | 0:Normal | 
Packet 20H

## Slide 94: PART 9: OBDH Critical TM
Parameter Number | Parameter Name | Work Range | Description
XS119 | Phased_array_antenna_working_timeout_Safety_Mode_Status | 0:Normal | 
XS120 | Phased_array_antenna_temperature_Safety_Mode_Status | 0:Normal | 
XS121 | CCD_temperature_Safety_Mode_Status | 0:Normal | 
XS122 | Energy_protect_Safety_Mode(triggered_by_TCU)_Status | 0:Normal | 
XS123 | Energy_warning_Safety_Mode_2_Status | 0:Normal | 
XS124 | Energy_warning_Safety_Mode_1_Status | 0:Normal | 
XS125 | AOCS_Stop_Control_Safety_Mode_Status | 0:Normal | 
XS126 | AOCS_Global_Attitude_Acquisition_Safety_Mode_Status | 0:Normal | 
XS127 | Energy_protect_Safety_Mode(triggered_by_PCU)_Status | 0:Normal | 
XS128 | TTD_Check_Error_Safety_Mode_Status | 0:Normal | 
XS129 | TTC_Check_Error_Safety_Mode_Status | 0:Normal | 
XS154 | Payload_Task_Protect_Safety_Mode_Status | 0:Not_happened | 
Packet 20H

## Slide 95: PART 9: OBDH Critical TM
Parameter Number | Parameter Name | Work Range | Description
XH140 | Time_calibration_with_GPS_ENABLE | 1:Enabled | 
XH164 | TTC_Check_Error_Safety_Mode_COUNTER | Don’ t Increase | 
XH165 | TTD_Check_Error_Safety_Mode_COUNTER | Don’ t Increase | 
XH166 | Energy_protect_Safety_Mode(_triggered_by_PCU)_COUNTER | Don’ t Increase | 
XH167 | AOCS_Global_Attitude_Acquisition_Safety_Mode_COUNTER | Don’ t Increase | 
XH168 | AOCS_Stop_Control_Safety_ModeCOUNTER | Don’ t Increase | 
XH169 | Energy_warning_Safety_Mode_1COUNTER | Don’ t Increase | 
XH170 | Energy_warning_Safety_Mode_2_COUNTER | Don’ t Increase | 
XH171 | Energy_protect_Safety_Mode(_triggered_by_TCU)_COUNTER | Don’ t Increase | 
XH172 | CCD_temperature_Safety_Mode_COUNTER | Don’ t Increase | 
XH173 | Phased_array_antenna_temperature_Safety_Mode_COUNTER | Don’ t Increase | 
XH174 | Phased_array_antenna_working_timeout_Safety_Mode_COUNTER | Don’ t Increase | 
XH175 | S-L_Separation_Switch_Timeout_Safety_Mode_COUNTER | Don’ t Increase | 
XH176 | TC_monitor_Timeout_Safety_Mode_COUNTER | Don’ t Increase | 
Packet 40H

## Slide 96: PART 10: In orbit operation
Daily operation:
KSM35-01 should be sent every day.
TC monitor Timeout Safety Mode will be triggered out if KSM35-01 is not received for 72 hours

## Slide 97: PART 10: In orbit operation
Phenomenon:
Satellite time be a small value, TTC buffer and TTD buffer is cleared (TTC number and TTD number become 0).
Possible cause:
OBC may reset or switch to the redundant part and recover data failed
Action：
Report DFH to deal with it

## Slide 98: PART 10: In orbit operation
Phenomenon:
Satellite time is normal, TTC Task Permission Status change to Disabled.
Possible cause:
Enter certain safe mode
Action：
Find which safe mode counter has changed, and report DFH to deal with it

## Slide 99: PART 10: In orbit operation
Phenomenon:
The TTC number dose not increase when inject TTC block from GS while XS001 has increased.
Possible cause:
The block format is wrong, or the block not satisfy insert rule, the time in the block conflicts with the time already in the satellite (Such as the same TTC block inject twice or more).
The TTC block is expired.
Action：
Check XS038 TTC insert status, if error, check which TTC blocks have been injected and their format.
If XS038 no error, Check if the time in the block is smaller than the time inject the block.
Report DFH, and DFH deal with it.
NOTE: XS038 will change from error to right when the right TTC block is injected.

## Slide 100: PART 10: In orbit operation
Phenomenon:
The TTD number dose not increase when inject TTD block from GS while XS001 has increased.
Possible cause:
The block format is wrong, or the TTD block not satisfy insert rule, the time in the block is conflict with the time already in the satellite ( Same TTD block inject twice or more often happen).
The TTD block is expired.
Action：
Check XS042 TTD update status, if error, check which TTD blocks have been injected and their format.
If XS042 no error, Check if the time in the block is smaller than the time inject the block.
Report DFH, and DFH deal with it.
NOTE: XS042 will change from error to right when the right TTD block is injected.

## Slide 101
Q & A?
THANKs FOR Your ATTENTION