## Slide 1
Inter-Satellite Laser
Communication
Design & Development of Optical Components
Dina | KAIST – Dept. of Aerospace Engineering | PhD Research Seminar
Link Budget
Optical Design
PAT Systems
WFE Budget
CubeSat OISL
Notes: Welcome slide. Introduce the topic: optical inter-satellite links as the key enabling technology for high-rate CubeSat constellations. Mention your research context at KAIST.

## Slide 2
AGENDA
What We Will Cover
01
Why Optical ISL?
Motivation & advantages over RF links
02
System Architecture
Terminal overview: TX chain, RX chain, PAT
03
Optical Components
Laser, modulator, telescope, FSM, detector
04
WFE Budget
Fabrication → thermal → dynamic contributors
05
PAT Control System
FSM tracking loop, Kalman filter, bandwidth
06
CubeSat Link Budget
Trade-space: aperture, range, data rate
Notes: Walk through the six major topics. Emphasize the connection: link budget drives component specs, which drive WFE budget, which feeds back into link margin.

## Slide 3
MOTIVATION
Why Optical ISL?
10–100×
Higher data rate
vs. Ka-band RF
~10 μrad
Beam divergence
(vs. ~1° for RF)
No ITU
Frequency
licensing needed
< 50%
Mass & aperture
vs. equivalent RF
RF limitations today
Ka-band ISLs: 100–600 Mbps, spectrum congested, large antennas, interference susceptible
Optical advantage
1550 nm laser: Tbps theoretical ceiling, diffraction-limited beam, inherent LPI/LPD for defense
CubeSat relevance
50 mm aperture OISL achieves Gbps at 500 km in a 0.5U volume — impossible with RF
Parameter | Ka-band RF | OISL 1550 nm
Data rate | 100–600 Mbps | 1–100 Gbps
Wavelength | 26–40 GHz | 1550 nm
Beam diverg. | ~0.5–2° | ~10–100 μrad
Aperture | 200–600 mm | 30–100 mm
Licensing | Required | None
Notes: Key message: optical ISL is not incremental — it is a paradigm shift in satellite communication. The beam narrowness is both the superpower (EM-quiet, compact) and the engineering challenge (PAT).

## Slide 4
SYSTEM OVERVIEW
Terminal Architecture
TX Chain
DFB seed laser (1550 nm, <100 kHz linewidth)
IQ / OOK / DPSK modulator
EDFA fiber amplifier (0.5–2 W)
Beam expander — Galilean afocal
Fine steering mirror (FSM)
RX Chain
Cassegrain or Dall-Kirkham telescope
Narrowband bandpass filter (0.3–1 nm)
InGaAs APD or SNSPD detector
Transimpedance amplifier (TIA)
DSP demodulator + FEC decoder
PAT Subsystem
2-axis coarse gimbal (±20–60°)
4-QD / CMOS beacon detector
FSM controller — PID + notch
Kalman state estimator
Acquisition scan algorithm
FSM is shared between TX pointing and PAT tracking loop — the actuator that steers the beam also closes the error correction feedback.
Notes: Emphasize the interdependence of the three chains — the FSM sits at the intersection of TX and PAT. The beacon detector feeds the pointing error that drives the FSM, which steers the TX beam. This tight coupling is the key design challenge.

## Slide 5
OPTICAL COMPONENTS — I
Laser Source & Modulator
Laser Source — MOPA Architecture
Wavelength
1550 nm (eye-safe, EDFA band)
Seed laser
DFB — linewidth < 100 kHz
Output power
10–40 mW seed → 0.5–5 W via EDFA
Coherence
Long coherence length for coherent Rx
Polarization
Linear — required for MZM modulator
RIN spec
< −150 dB/Hz for high-SNR links
Space qual.
Radiation-hardened Er-doped fiber
Modulation Formats
OOK
On-Off Keying
Simple, robust
Sensitivity: ~−28 dBm @ 10G
DPSK
Diff. Phase Shift Keying
+3 dB vs OOK
Sensitivity: ~−31 dBm @ 10G
QPSK
Quad Phase Shift Keying
Coherent Rx needed
Sensitivity: ~−35 dBm @ 10G
Doppler challenge @ 1550 nm: two LEO satellites at 7.5 km/s → ~5 GHz Doppler shift → requires optical pre-compensation in the PAT loop.
Notes: The MOPA architecture is standard because it separates frequency stability (DFB seed) from power (EDFA). The Doppler shift at 1550 nm is enormous compared to RF — 5 GHz compared to a few MHz for Ka-band — and must be managed in the tracking/control loop.

## Slide 6
OPTICAL COMPONENTS — II
Beam Expander & Fine Steering Mirror
Beam Expander (Transmit Telescope)
Type:
Galilean afocal (no focal point — no air breakdown at high power)
Aperture D:
30–80 mm, CubeSat constrained to ~50 mm
Divergence:
θ ≈ λ/(π·w₀) → ~40 μrad for 50 mm @ 1550 nm
Footprint @ 500 km:
~20 m beam diameter (vs. 4 km for Ka)
Wavefront req.:
Strehl > 0.8 → WFE < λ/14 = 111 nm RMS
Thermal design:
Zerodur/fused silica; bipod flexure mounts for athermal
AR coatings:
< 0.25% reflectance; no back-reflection to EDFA
Fine Steering Mirror (FSM)
Aperture:
15–30 mm clear aperture
Actuation:
PZT stacks (high BW) or VCA (large stroke)
Range:
±1–5 mrad, covers residual post-gimbal error
Resolution:
< 1 μrad per step (PZT charge-mode drive)
Bandwidth:
> 500 Hz to reject RW harmonics
Hysteresis:
15% (voltage mode) → < 1% (charge mode)
Function:
TX beam steering + PAT error correction (same actuator)
Key coupling: divergence θ ∝ λ/D → larger aperture = narrower beam = higher gain = tighter pointing requirement.
Notes: The Galilean beam expander avoids a focal point inside the optics — important when multi-watt beams could ionize air or damage coatings at a focus. The FSM is unique because it is shared hardware between TX beam-steering and PAT error correction.

## Slide 7
OPTICAL COMPONENTS — III
Receive Telescope & Photodetector
InGaAs APD
Workhorse for LEO-LEO OISL
Internal gain M = 5–20×
Sensitivity: −30 to −35 dBm @ 10G
Operates at room temperature
InGaAs sensitive 900–1650 nm
SNSPD
Deep-space / photon-starved links
Single-photon sensitivity, >90% efficiency
Timing jitter < 50 ps
Used in NASA LLCD (lunar demo)
Complete Receive Chain
Cassegrain
Telescope
50–100 mm
D_rx aperture
Bandpass
Filter
0.3–1 nm
passband
Focus
Optics
f/4–f/8
focal ratio
APD
Detector
InGaAs
M = 10–15
TIA + DSP
Demod +
FEC
Notes: For CubeSat OISL, APD is the only realistic choice — SNSPDs require cryogenic cooling at 4K which is incompatible with a 10W CubeSat power budget. The bandpass filter is critical: without it, solar background at 1550nm would saturate the APD.

## Slide 8
WAVEFRONT ERROR BUDGET
From Surface to Strehl
Maréchal Approximation
S ≈ exp[−(2π·σ/λ)²]
Primary mirror surface figure
11 nm
Secondary mirror figure
8 nm
Relay lens transmitted WFE
6 nm
AR/HR coating micro-roughness
4 nm
Mirror decenter (assembly)
9 nm
Axial despace / focus error
7 nm
Thermal gradient — mirror deformation
12 nm
Mounting stress (flexures)
6 nm
Residual vibration post-FSM
4 nm
0
5
10
15
20
nm RMS
RSS Total WFE: 23.7 nm
Strehl S ≈ 0.91 → Diffraction-limited (S > 0.8 criterion)
Notes: RSS combination assumes statistically independent contributors. Thermal gradient dominates at 12nm — drives material selection (Zerodur, fused silica) and thermal control design. Budget target was S > 0.80; achieved S = 0.91 with margin.

## Slide 9
WFE DESIGN PROCESS
From Requirement to Hardware
1
System Strehl requirement
Derive from link budget: max allowable coupling loss → min Strehl → max RSS WFE. Set target to 70% of limit for margin.
2
Zemax sensitivity analysis
Perturb each element in 6 DOF. Compute S_ij = ∂WFE_i/∂DOF_j matrix. Identifies dominant sensitivity (e.g., secondary decenter → coma).
3
WFE allocation
Invert sensitivities: δ_j = σ_i / S_ij gives mechanical tolerance per DOF. Iterate until tolerances are achievable with available mechanisms.
4
Manufacture & metrology
Fizeau interferometry measures surface figure (λ/50 figure = ~10 nm RMS). Ion-beam polishing for final correction. Zygo/4D Technology instruments.
5
Space qualification
Thermal vacuum cycling (−40°C to +70°C), random vibration, shock, TID radiation. EDFA/DFB aging tests for mission life.
6
End-to-end link test
Hardware-in-the-loop with turbulence emulator, range-equivalent attenuation. Validates integrated performance before spacecraft integration.
Notes: The development process is inherently iterative — sensitivity analysis feeds back into optical design, and tolerance results feed into mechanical design. This matrix-driven approach is how professional space programs (ESA, NASA) manage optical budgets.

## Slide 10
PAT CONTROL SYSTEM
FSM Tracking Loop Design
FSM Plant Model P(s)
P(s) = K_act · ω_n² / (s² + 2ζω_n·s + ω_n²)
ω_n = 2π×500–2000 rad/s | ζ = 0.01–0.05 (lightly damped) | K_act = 10–50 μrad/V
Controller C(s) = PID × Notches
C(s) = K_p (1 + 1/T_i·s + T_d·s/τ) · N_res(s) · N_RW(s)
Loop crossover f_c ≈ 300 Hz | Phase margin ≥ 45° | Gain margin ≥ 6 dB
4-Quadrant Detector
Bandwidth: up to 100 kHz
Linear range: ±20% spot diameter
Ideal for fine-tracking phase
CMOS Focal Array
Wide linear FOV
Latency = 1 frame period
Phase lag: 360°·f_c/f_frame
Kalman Estimator
Estimates jitter state
Disturbance feed-forward
Cancels RW harmonics predictively
Notch Filter:
N(s) = (s² + 2ζ_z·ω_n·s + ω_n²) / (s² + 2ζ_p·ω_n·s + ω_n²) with ζ_z = 0.001 (deep null at mechanical resonance), ζ_p = 0.3–0.5 (wide denominator to restore phase)
Notes: Key insight: the notch filter is not optional — without it the PID controller would excite the mechanical resonance and oscillate. The Kalman filter upgrade provides ~10 dB additional disturbance rejection over plain PID by predicting and canceling reaction-wheel harmonics.

## Slide 11
LINK BUDGET
CubeSat OISL Trade-Space
P_rx = P_tx · η_tx · (π D_tx² / 4λ²) · (π D_rx² / 4R²) · η_rx · L_point
TX power at aperture
0.5 W
+27.0 dBm
TX optical efficiency η_tx
0.75
−1.2 dB
TX aperture gain G_tx
D=40mm
+76.8 dB
Free-space path loss
500 km
−278.2 dB
RX aperture effective area
40mm
+67.2 dB
RX optical efficiency η_rx
0.60
−2.2 dB
Pointing loss
2 dB est
−2.0 dB
Received power
−112.6 dBm
−41 dBm
APD sensitivity
@ 1 Gbps
+28 dB
Link margin
(above Gbps threshold)
~3 Gbps
Max data rate
at these params
Notes: The free-space path loss at 500 km at 1550 nm is ~278 dB. The TX aperture gain at 40mm is ~77 dB — this is why optical beats RF so decisively. The link margin of ~28 dB gives enormous headroom for pointing losses and hardware variation.

## Slide 12
TRADE-SPACE ANALYSIS
Aperture × Range × Data Rate
Chart: Max Data Rate (Mbps) vs. Range (km)
| 100 | 300 | 500 | 700 | 1000 | 1500
D = 20 mm | 520 | 58 | 21 | 11 | 5 | 2.4
D = 40 mm | 8300 | 920 | 330 | 170 | 83 | 37
D = 60 mm | 42000 | 4600 | 1660 | 840 | 420 | 185
P_rx ∝ D⁴
Both TX and RX aperture scale the received power — doubling aperture on both sides = 12 dB gain (×16 in power).
P_rx ∝ 1/R²
Classic free-space spreading — doubling range costs 6 dB. At 1000 km, margin drops 6 dB vs. 500 km.
CubeSat limit
1U constrains aperture to ~40–50 mm. This limits practical Gbps+ links to < 800 km range with 0.5W TX.
Power tradeoff
EDFA at 1W output consumes ~5–8W DC power — 50–80% of a 10W CubeSat budget. Dominant system constraint.
Notes: The D⁴ scaling is the most important insight: since both TX and RX aperture enter as D², using matched apertures means received power scales with D⁴. This is why aperture selection is the highest-leverage design choice in CubeSat OISL.

## Slide 13
PAT — ACQUISITION
From Blind to Locked: 3-Stage PAT
Stage 1: Coarse Acquisition
Uncertainty: ±0.05–0.5°
(from star tracker ephemeris)
Wide-divergence beacon laser (980 nm, 5–10° half-angle) transmitted from both terminals. CMOS wide-FOV detector (1–10°) scans angular uncertainty cone. Ephemeris-based pointing prediction narrows cone. Time: 1–30 sec.
After: error reduced from ~500 mrad to < 5 mrad
Stage 2: Intermediate Lock
Uncertainty: ±1–5 mrad
(post gimbal settle)
Coarse gimbal steers bore-sight to place partner's beacon on fine tracking detector. 2-axis motorized mechanism with ±20–60° travel and ~1 mrad resolution. Closed-loop gimbal controller reduces error. Time: 0.1–2 sec.
After: error reduced to < 500 μrad (FSM range)
Stage 3: Fine Tracking Lock
Uncertainty: < 500 μrad
(FSM handles)
FSM takes over: 4-QD or CMOS beacon detector feeds pointing error to PID+Kalman loop. FSM nulls error to < 5 μrad RMS. Data channel opens. Link active. Time: < 100 ms.
After: pointing error < 5 μrad → data link open
→
→
Notes: The three-stage acquisition is driven by the enormous mismatch between initial pointing uncertainty (0.5°) and beam divergence (40 μrad = 0.002°). A single-stage direct acquisition would require sweeping 625,000 beam positions — practically impossible in real time.

## Slide 14
CUBESAT OISL — CONSTRAINTS & FRONTIERS
Engineering Tensions & Research Directions
Volume
50 mm aperture Cassegrain: 150–400 g, ~0.5U volume. Every mm of aperture is contested.
Power
EDFA @ 1W optical output = 5–10W DC. This is 50–80% of a 10W CubeSat power budget.
Mass
Gimbal mechanism 100–300 g. Primary mass driver after telescope. Drives to MEMS solutions.
Thermal
Orbit ΔT ±50°C. Athermal design mandatory. Zerodur or titanium-mounted fused silica.
Active Research Frontiers
MEMS FSM
MEMS FSM:
Micro-electromechanical steering mirrors: sub-gram, < 1 cm², 10 kHz bandwidth. Replace macroscopic PZT mechanisms entirely.
Photonic ICs
Photonic ICs:
InP/Si PIC transceivers integrate laser + modulator + APD on a single chip. Enables < 5 cm³ transmit chain.
Diffractive optics
Diffractive optics:
Diffractive beam expanders and gratings reduce element count, mass, and volume vs. refractive or reflective systems.
Coherent QPSK
Coherent QPSK:
Higher spectral efficiency enables Gbps+ at longer range or smaller aperture. Requires DSP Doppler compensation.
Notes: This slide bridges the tutorial into your own research context. MEMS FSM and PIC transceivers are the two technologies most likely to enable true 1U CubeSat OISL within 5 years.

## Slide 15
CONCLUSION
Key Takeaways
01
OISL achieves 10–100× higher data rate than Ka-band RF with smaller apertures — enabled by the λ = 1550 nm coherent beam physics.
02
The link budget governs everything: P_rx ∝ D⁴ means aperture is the highest-leverage design variable. Every mm counts in CubeSat form factor.
03
WFE budget builds from λ/50 polished optics through assembly tolerances and thermal deformation to achieve Strehl > 0.8 (S ≈ 0.91 in our design).
04
The FSM tracking loop (PID + notch filters, > 500 Hz bandwidth, Kalman estimator) is the critical control subsystem — PAT is the dominant engineering challenge.
05
CubeSat-scale OISL (< 50 mm aperture, < 1W TX, 1U volume) enables Gbps+ links at < 800 km — feasible today. Frontier work: MEMS FSM, PIC transceivers.
KAIST · Dept. of Aerospace Engineering · PhD Research Seminar · 2026
Notes: Close with the connection to your own research: your hall-thruster optimization work for CubeSat propulsion and the OISL link design for inter-satellite data relay are the two technical pillars of a 1U platform with full mission capability.